European Radiocommunications Committee (ERC)

within the European Conference of Postal and Telecommunications Administrations (CEPT)

European Radiocommunications Committee (ERC)

within the European Conference of Postal and Telecommunications Administrations (CEPT)

FURTHER SHARING STUDY BETWEEN THE FIXED SERVICE AND
EARTH EXPLORATION-SATELLITE SERVICE IN THE BAND 55.22 - 55.78 GHz

Sesimbra, January 1997

TABLE OF CONTENTS

1	INTRODUCTION	1

2	PASSIVE SENSORS	1

2.1	Introduction	1

2.2	Significance of passive measurements performed by the EESS near the  resonance frequencies                            around 60 GHz	1

2.3	Current and future satellite systems and instrumentation	2

2.3.1	Satellite systems	2

2.3.2	Instrumentation	2

2.3.3	Typical characteristics of microwave sounders	3

2.4	Interference criteria for passive sensors, and vulnerability to interference	3

2.4.1	Current interference criteria definition	3

2.4.2	Vulnerability to interference	3

2.5	Interference classification	4

2.6	Sharing conditions	4

3	REQUIREMENTS FOR FIXED SERVICES	7

3.1	Introduction	7

3.2	Terrestrial Propagation in the Millimetric Wavebands	7

3.3	Current and Future Use of the Oxygen Absorption Band by the Fixed Service	8

3.4	ETSI Standards Under Development	8

3.5	Fixed Service System Parameters	9

3.6	FS transmitter output power	9

3.7	Possible Means of Sharing	9

4.	IMPLICATIONS FOR SHARING IN THE BAND 55.22 - 55.78 GHz	10

4.1	Direct Interference Propagation Path	10

4.2	Indirect Interference Propagation Path	12

4.3	Effect of Antenna Elevation	13

5.	CONCLUSIONS	14

LEFT BLANK

SHARING BETWEEN THE FIXED SERVICE AND
EARTH EXPLORATION SATELLITE SERVICE IN THE BAND 55.22 - 55.78 GHz

1	INTRODUCTION

ERC Report 45 contains an examination of the feasibility of sharing between the fixed service (FS) and Earth exploration-satellite service (EESS) in the range 50.2 to 58.2 GHz.  This report concludes that sharing between passive remote sensors and the fixed service is feasible between 55.78 and 58.2 GHz, but not feasible between 50.2 and 55.22 GHz; in the initial study there was no definitive conclusion on the feasibility of sharing in the range 55.22 - 55.78 GHz.  The following report contains the results of further studies focusing in particular on the band 55.22 - 55.78 GHz

2	PASSIVE SENSORS

2.1	Introduction

The electromagnetic spectrum contains many frequency bands where, due to molecular resonances, absorption mechanisms by certain atmospheric gases are taking place.  Frequencies at which such phenomena occur characterise the gas.  The absorption coefficient depends on the nature of the gas, on its concentration, and on its temperature. A combination of passive measurements around these frequencies can be performed from spaceborne platforms, to retrieve temperature and/or concentration profiles of absorbing gas.  Of particular significance to the EESS below 200 GHz are the oxygen resonance frequencies between 50 and 70 GHz, and at 118.75 GHz, and the water vapour resonance frequencies at    22.235 GHz and at 183.31 GHz.

A general view of the atmospheric attenuation due to oxygen and water vapour at frequencies up to 350 GHz is shown in Figure 1.

Detailed oxygen absorption spectrum in the vicinity of 60 GHz is shown in Figure 2.  The two neighbouring absorbing peaks which limit the frequency slot under consideration in this document are also indicated.

2.2	Significance of passive measurements performed by the EESS near the  resonance frequencies around       60 GHz

Spaceborne microwave passive sounders making passive measurements near the resonance frequencies around 60 GHz are deployed, particularly by the meteorological services.  Their purpose is to provide on a worldwide basis “all weather” three dimensional measurements of the temperature profiles, key parameters which describe the status of the atmosphere.

Temperature profiles are among the few essential parameters describing the status of the atmosphere, which are fed directly into the operational Numerical Weather Prediction models (NWP) operated by the meteorological services.

Weather forecasting is a “Public Service” which leads to significant economic benefits for most human activities such as agriculture, transport, construction, energy production etc, and contributes also to protect human lives and properties.  There is a strong demand for improvements of this service, particularly in accuracy and in reliability.

All weather atmospheric temperature profiles are also essential for scientific applications such as climate and environment monitoring (“Global change” for example).  They are also the key auxiliary parameter, which is necessary to extract the concentration profiles of radiatively and chemically important atmospheric gases (such as ozone), from radiometric measurements in their specific absorption bands.

Compared to infra-red (IR) techniques, the all-weather capability (the ability for a spaceborne sensor to “look” through most clouds) is probably the most important feature that is offered by microwave techniques.

This is fundamental for operational weather forecast and atmospheric science applications, because more than 60% of the earth's surface, on average, is totally overcast by clouds, and only 5% of all 20x20 km pixels  (corresponding to the typical spatial resolution of the IR sounders) are completely cloud-free.  This situation severely hampers operations of IR sounders, which have very little or no access to large, meteorologically active regions.

High resolution all-weather temperature profiles can only be obtained by passive measurements from low-earth polar orbiting satellites within the oxygen absorption spectrum around 60 GHz.  High vertical resolution is rendered possible by the multi-line structure of the absorption spectrum.

Because of its specific absorption level, the 55.22 - 55.78 GHz sub-band is the only suitable one in the spectrum where tropopause information can be collected, as for example by the AMSU-A channel 8 (as shown in Figure 3). This is a unique natural resource for which no alternative exists.

2.3	Current and future satellite systems and instrumentation

2.3.1	Satellite systems

Meteorological services operate essentially two complementary types of satellite systems:

-	Systems based on satellites in low sun-synchronous polar orbits are used to acquire high resolution environmental data on a global scale.  The repeat rate of measurements is limited by the orbital mechanics.  A maximum of two global coverages are obtained daily, with one single satellite.

Two low orbiting meteorological satellites in coordinated orbits (“morning” and “afternoon”) are currently operated by NOAA (NOAA-K/L/M/N/N’, USA).  This network yields one complete coverage every 6 hours on average.  NOAA-M, to be launched in 1999, will be the last “morning” satellite of the series.  Consequently, Europe (ESA and EUMETSAT) has accepted to take up the responsibility of a “morning” satellite system, “METOP”, which will be developed in Europe.  The first satellite of this European series is planned to be launched in 2002;

-	Systems involving satellites in geostationary orbit are used to gather low to medium resolution data at regional scale.  The repeat rate of measurements is limited only by hardware technology, and is typically one regional coverage every 30 minutes or less.

Five to six geostationary meteorological satellites regularly spaced around the earth’s equator are deployed.  The European component, METEOSAT, is positioned at 0° longitude.

2.3.2	Instrumentation

Since 1978, the Meteorological Satellite Service has used sections of the oxygen absorption spectrum around 60 GHz for passive microwave sounding of the atmosphere.  These measurements are provided by the Microwave Sounding Unit (MSU) instrument which is flown on the operational series of polar-orbiting weather satellites operated by NOAA.  MSU is a 4 channel radiometer.

On the basis of experience gained with the MSU data, NOAA is going to upgrade the microwave sounding capability on its operational polar-orbiting satellites in the near future.  This capability will be provided by two new instruments:

-	The Advanced Microwave Sounding Unit - A (AMSU-A), for determining atmospheric temperature profiles, has 15 channels of which 12 channels fall within the 50.2 - 58.2 GHz band;

-	The Advanced Microwave Sounding Unit - B (AMSU-B, supplied by the UK), for determining atmospheric water vapour profiles, has 5 channels of which 3 channels fall around 183.31 GHz.

The first flight of the AMSU-A and AMSU-B instruments, on the NOAA-K/L/M/N/N’ series, is currently scheduled for the end of 1996.  The AMSU-A is also going to fly on the European satellite series METOP.

Further upgrading of the microwave sounding capability will be achieved:

-	In the 2005 timeframe, “stratospheric” channels in the frequency range 60.3 - 61.3 GHz, will be added to the AMSU-A instrument.  Such channels will increase the maximum height at which the atmospheric temperature is retrieved from approximately 45 km to approximately 70 km.  This technique relies on a special interaction between the Earth's magnetic field and particular O2  absorption lines (“Zeeman splitting”).

-		In the 2002 timeframe, on the METOP satellite, the water vapour sounding capability will be ensured by the Microwave Humidity Sounder (MHS), an improved version of the AMSU-B, which is being developed in Europe.  The MHS may replace the AMSU-B on the NOAA-N and N’ “afternoon” satellites.

A number of other microwave sounding instruments using similar frequency bands are also in operation, in particular on US military weather satellites, and on Russian weather satellites.

Due to technological constraints, no microwave sounder has been flown as yet on a geostationary meteorological satellite.  This is however envisaged on future systems.  Microwave sounders for geostationary platforms will have channels around 183.31 GHz for water vapour profiling, as for the instruments in low earth orbits.  For temperature profiling, the 118.75 GHz region is preferred over the 60 GHz in order to minimise the size of the antenna.

2.3.3	Typical characteristics of microwave sounders

|  | Present : | Future : |
| --- | --- | --- |
| Antenna diameter : IFOV 3dB points : FOV (cross-track) : Antenna gain : Side lobes : Beam efficiency : Radiometric resolution : Swath width : Pixel size (nadir) : Number of pixels/line : Orbit altitude (circular) : Orbit inclination (sun-synchronism) : | 15 cm 3.3° +/- 50° 36 dBi - 10 dBi > 95% 0.3 K 2300 km 49 km 30 850 km 98.8 ° | 45 cm 1.1° +/- 50° 45 dBi -10 dBi > 95 % 0.1 K 2300 km 16 km 90 850 km 98.8 ° |

2.4	Interference criteria for passive sensors, and vulnerability to interference

2.4.1	Current interference criteria definition

Recommendation ITU-R SA 1029 sets the permissible interference threshold as follows: