Normative part

| Nr | Parameter | Description | Comments |
| --- | --- | --- | --- |
| 1 | Radiocommunication Service | Mobile service Fixed service |  |
| 2 | Application | DECT |  |
| 3 | Frequency band | 1880-1900 MHz |  |
| 4 | Channelling | Not specified. DECT equipment must be compliant with EN 301 406 |  |
| 5 | Modulation / Occupied bandwidth | Not specified. DECT equipment must be compliant with EN 301 406 |  |
| 6 | Direction / Separation | Not specified DECT equipment must be compliant with EN 301 406 |  |
| 7 | Transmit power / Power density | nominal transmit power of up to 250 mW (24 dBm) and equivalent isotropic radiated power (EIRP) of up to 26 dBm for omni-directional antennas and 30 dBm for directional antennas; |  |
| 8 | Channel access and occupation rules | Not specified DECT equipment must be compliant with EN 301 406 |  |
| 9 | Authorisation regime | DECT equipment compliant with the specified usage conditions is exempted from individual licensing |  |
| 10 | Additional essential requirements according to Art. 3.3 of R&TTE Directive | None |  |
| 11 | Frequency planning assumptions | Residential and enterprise equipment is mainly installed indoors and base stations for coverage of onsite related outdoor areas are intended to be installed below rooftop and below 7 m | ETSI TR 103 089 (V1.1.1 (2013-1) states the following: “The mandatory Instant Dynamic Channel Selection (iDCS) messages and procedures provide effective co-existence of uncoordinated private and public systems on the common designated DECT frequency band and avoid any need for traditional frequency planning.” |

Informative Part

| Nr | Parameter | Description | Comments |
| --- | --- | --- | --- |
| 12 | Planned changes |  |  |
| 13 | Reference | ERC/DEC/(98)22 The frequency band 1880-1900 MHz is designated for DECT by ERC/DEC/(94)03 |  |
| 14 | Notification number |  |  |
| 15 | Remarks |  |  |