BORDER CODE COORDINATION BETWEEN CDMA2000 SYSTEMS IN 450 MHz BAND

Vienna, October 2007

# EXECUTIVE SUMMARY

This report has been completed to complement existing ECC Report 97 “Cross Border Interference for Land Mobile Technologies” and ERC Recommendation T/R 25-08 “Planning Criteria and Coordination of Frequencies in the Land Mobile Service in the Range 29.7-921 MHz” and addresses the issue of code coordination between CDMA systems based on CDMA 2000 interface. The guidance in this report is directed to Administrations wishing to develop such CDMA systems in their countries.

The report studies applicability of the code coordination approach used in ERC Recommendation 01-01 “Border Coordination of UMTS/IMT-2000 Systems” to CDMA systems based on CDMA2000 interface. Due to similarity of CDMA interfaces the same code allocation scheme could be used for CDMA-PAMR and CDMA-450 systems coordination tacking into account CDMA2000 codes hierarchy. The threshold levels of the predicted mean field strength for coordination are deduced from ECC Report 97 “Cross Border Interference for Land Mobile Technologies” and analysis provided in this report. ECC Report 97 contains the results of Monte Carlo simulations of CDMA-PAMR networks using SEAMCAT software.

This report is relevant only for cases when neighboring Administrations use or plan to use CDMA2000 networks on their territory and their frequency plans coincide. For other cases ERC Recommendation T/R 25-08 should be referenced.

TABLE OF CONTENTS

0	EXECUTIVE SUMMARY	2

1	INTRODUCTION	3

2	Code allocation scheme	3

3	coordination thresholds	3

4	conclusions	3

5	BIBLIOGRAPHY	3

ANNEX 1: Tables with correlation area percentage (geometrical approach)	3

ANNEX 2: Tables with correlation area percentage (propogation approach)	3

Border Code Coordination between CDMA-PAMR Systems

# INTRODUCTION

This report addresses the issue of cross border coordination between CDMA2000 systems with code coordination procedure. The guidance in this report is directed to Administrations wishing to develop CDMA systems based on CDMA 2000 interface in their countries. This report is applicable only for code coordination between CDMA2000 systems which frequency plans coincide.

Recommendation and report have addressed the issue of cross border coordination for Land Mobile service:

- ECC Report 97 “Cross Border Interference for Land Mobile Technologies”;

- ERC Recommendation T/R 25-08.

ECC Report 97 “Cross Border Interference for Land Mobile Technologies” and ERC Recommendation T/R 25-08 provides procedures and thresholds for coordinated cases, for preferential and non-preferential allocation cases for different Land Mobile technologies including CDMA-PAMR. However data presented in these documents considers the case for CDMA networks when both systems use aligned frequencies with already coordinated codes. But uncoordinated case with CDMA systems using aligned frequencies isn’t considered in any ECC document. To investigate this case and provide possible variant of code coordination procedure this report is prepared. The baseline for such procedure could be found in ERC Recommendation 01-01 where code coordination between UMTS systems is described. For code coordination it is proposed to deduce threshold levels partly from ECC Report 97 “Cross Border Interference for Land Mobile Technologies” and partly from the proposed simplified model of uncoordinated CDMA networks.

# Code allocation scheme

For code coordination each base station shall use a unique time offset of the pilot pseudonoise (PN) sequence to identify a Forward CDMA Channel. Time offsets may be reused within a CDMA cellular system. Distinct pilot channels shall be identified by an offset index (0 through 511 inclusive). This offset index specifies the offset time from the zero offset pilot PN sequence in multiples of 64 chips. The same pilot PN sequence offset shall be used on all CDMA frequency assignments for a given base station. To distinct signals with PN sequence offsets all base stations should be time synchronized but such synchronization is mandatory requirement for CDMA2000 standard.

Administrations should agree on a repartition of these offset indexes on an equitable basis. In any case, each country can use all codes in the most important part of its own territory.

In border areas, codes will be divided into 6 "index sets" containing each one sixth of the available offset indexes. Each country is allocated three index sets (half of the indexes) in a bilateral case, and two index sets (one third of the indexes) in a trilateral case.

Four types of countries are defined in a way such that no country will use the same index set as any one of its neighbours. The following lists describe the distribution of European countries:

Type country 1: BEL, CVA, CYP, CZE, DNK, E, FIN, GRC, IRL, ISL, LTU, MCO, SMR, SUI, SVN, UKR, AZE, SRB.

Type country 2: AND, BIH, BLR, BUL, D, EST, G, HNG, I, MDA, RUS (Exclave), GEO

Type country 3: AUT, F, HOL, HRV, MKD, POL, POR, ROU, RUS, S, MLT

Type country 4: ALB, LIE, LUX, LVA, MNE, NOR, SVK, TUR.

For each type of country, the following tables and figure describe the sharing of the indexes with its neighbouring countries, with the following conventions of writing:

|  |  | Preferential index |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | non-preferential index |  |  |  |  |  |  |

|  | Set A | Set B | Set C | Set D | Set E | Set F |  |  | Set A | Set B | Set C | Set D | Set E | Set F |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Country 1 | 2..83 | 88..168 | 173..253 | 258..338 | 343..423 | 428..509 |  | Country 2 | 2..83 | 88..168 | 173..253 | 258..338 | 343..423 | 428..509 |
| Border 1-2 |  |  |  |  |  |  |  | Border 2-1 |  |  |  |  |  |  |
| Zone 1-2-3 |  |  |  |  |  |  |  | Zone 2-3-1 |  |  |  |  |  |  |
| Border 1-3 |  |  |  |  |  |  |  | Border 2-3 |  |  |  |  |  |  |
| Zone 1-2-4 |  |  |  |  |  |  |  | Zone 2-1-4 |  |  |  |  |  |  |
| Border 1-4 |  |  |  |  |  |  |  | Border 2-4 |  |  |  |  |  |  |
| Zone 1-3-4 |  |  |  |  |  |  |  | Zone 2-3-4 |  |  |  |  |  |  |
|  | Set A | Set B | Set C | Set D | Set E | Set F |  |  | Set A | Set B | Set C | Set D | Set E | Set F |
| Country 3 | 2..83 | 88..168 | 173..253 | 258..338 | 343..423 | 428..509 |  | Country 4 | 2..83 | 88..168 | 173..253 | 258..338 | 343..423 | 428..509 |
| Border 3-2 |  |  |  |  |  |  |  | Border 4-1 |  |  |  |  |  |  |
| Zone 3-1-2 |  |  |  |  |  |  |  | Zone 4-1-2 |  |  |  |  |  |  |
| Border 3-1 |  |  |  |  |  |  |  | Border 4-2 |  |  |  |  |  |  |
| Zone 3-1-4 |  |  |  |  |  |  |  | Zone 4-2-3 |  |  |  |  |  |  |
| Border 3-4 |  |  |  |  |  |  |  | Border 4-3 |  |  |  |  |  |  |
| Zone 3-2-4 |  |  |  |  |  |  |  | Zone 4-3-1 |  |  |  |  |  |  |

Figure 1

Because of time shifting mechanism for code generation, the situation when propagation delay may lead to synchronisation of two different base stations signals occurring in some parts of service area. The average diameter of such correlation areas could be up to 245 meters (one chip duration multiplied on light speed). To prevent such situations in border areas it is recommended not to use some codes and to introduce 4 exclusion codes between neigboring index sets what gives 78.125 km propagation path before possible correlation area appears. This precludes any real synchronisation and reduction of code space less than on 5% only in border areas won’t affect network planning.

All codes are available in areas away from the border where the field strengths into the neighbouring country are below the relevant trigger levels.

A two countries code sharing should be applied or used by base stations that exceed the relevant trigger level (Item 3) of only one neighbouring country. A three countries code sharing should be applied or used by base stations that exceed the relevant trigger level (Item 3) of two neighbouring countries.

In certain specific cases (e.g. AUT/HRV) where the distance between two countries of the same Type number is very small (< few 10s km), it may be necessary to address the situation in bi/multilateral coordination agreements as necessary, and may include further subdivision of the allocated codes in certain areas.

# coordination thresholds

Two types of thresholds should be specified:

- trigger level of the predicted mean field strength on the border  to perform code coordination for exact base station, which also correspond to maximum permitted level of the mean field strength on the border for base stations using non-preferential codes;

- maximum permitted level of the mean field strength on the border for base stations using preferential codes.

ECC Report 97 provides maximum permitted level of the mean field strength on the border for CDMA-PAMR base stations for coordinated case when both systems use aligned frequencies and preferential codes. It is proposed to use this level as the maximum permitted level for the case of BS using preferential codes. The deduction layout from ECC Report 97 relevant to this issue is explained below.

To define threshold level for cross border operation of CDMA systems in coordinated case a new principle was proposed which states that a network should not be protected to a greater extent than it would be from its own continuously rolled out network. The studies were undertaken using Monte Carlo modelling. The two CDMA systems were modelled at separation distances which were progressively increased.

Figure 3

The outage of users in reference cell with permanent capacity was taken as the criteria of coexistence. Nominal outage and nominal capacity was obtained from the modelling of the cell in the completely rolled out network. Then the network was divided in two and only one part was left what caused reduction of self-interference and consequently reduction of outage. Interfering network is situated such way that produces the exact level of interference to return outage to its nominal value. The power level in the middle of separation distance is taken as threshold on the border. Only downlink to downlink case was considered as the worst case.

The permissible interference for duplex technologies was measured in a bandwidth of 25 kHz at a height of 3 metres in 50% of time. The result shown in the study for two CDMA systems is -104.1 dBm. Modelling was undertaken at 450 MHz but the results are applicable over the range of frequencies used by CDMA2000 based systems below 1000 MHz. For the studies in  ECC Report 97 the Extended Hata model for subrural environment was used.

Thresholds for duplex systems should be based on the power measured in a 0 dBi antenna, these may be converted to field strengths (as dBuV/m) at the appropriate frequency. The use of a 0 dBi antenna, as a standard for comparison, represents a worst case, particularly at lower frequencies, where 0 dBi antennas are less common. The formula for the conversion of dBm to dBuV/m is:

FdBuV/m = PdBm + 77.21 + 20lg(fMHz)

where PdBm is the power in dB microwatts.

The calculation of relevant field strength level in case of aligned frequencies and preferential codes for CDMA2000 in 450 MHz band is presented below:

| Central frequency of downlink band | Threshold field strength level on the border (rounded)* | Overall CDMA BS signal strength on the border** |
| --- | --- | --- |
| 465 MHz | 26.5 dBuV/m/ 25 kHz | 43.5 dBuV/m/ 1.25 MHz |

Table 1

* - measured in a bandwidth of 25 kHz at a height of 3 metres in 50% of time.

**- measured in a bandwidth of 1250 kHz at a height of 3 metres in 50% of time (recommended).

SEAMCAT model, which was used for cross border studies, is not applicable for uncoordinated case with aligned frequencies because each CDMA receiver in SEAMCAT applies processing gain only to its wanted signal. It is difficult to define accurately real correlation zones because of multi-pass propagation when different delays could occur. Theoretically it could occur almost at any location within victim cell. But to estimate the impact of possible correlation between different BS signals on network performance simplified model is proposed with line-of-sight conditions. To find areas of possible correlation the geometrical problem should be solved. The areas where the following conditions are true should be defined as:

Ri-15.625-0.120≤Rv≤ Ri-15.625+0.120 (correlation with the adjacent PN offset)

Ri-2*15.625-0.120≤Rv≤ Ri-2*15.625+0.120 (correlation with the second adjacent PN offset)

Ri-3*15.625-0.120≤Rv≤ Ri-3*15.625+0.120 (correlation with the third adjacent PN offset).

Where Ri is the distance from interfering BS and Rv is the distance from investigated victim BS. All areas are limited to victim cell circle. The case of same PN offset interference is possible only for overlapping cells which is improbable for cross border situation and not defined in the above conditions. The geometrical networks representation for estimating such areas is shown below. 5.9 km cell radii and omni antennas were considered which is in agreement with parameters used in cross border study.

Figure 4

Different interfering cells create different impact in victim cells. For one fixed separation distance there could be up to 19x19=361 different area projections. Some examples of such potential correlation areas for 20 km separation are presented below.

Figure 5

To provide wide range of results for different separation distances it is easier to present only cell area percent relevant to correlation zone (100% correspond to the circle area defined by cell radii). Set of tables for all combination of interfering and victim cells for separation distances from 12 to 50 km is attached in the Annex 1.

Next step is to look on the impact in terms of propagation. It is likely to have harmful interference at the edge of the cell and unlikely to have any interference near wanted BS. Also the magnitude of the impact is very dependent both on path losses between wanted Tx and victim Rx and path losses between interfering Tx and victim Rx. It is proposed to look at the worst case when path loss between wanted BS and victim Rx is approximated with Hata suburban model and pass loss between interfering BS and victim Rx is approximated with Hata rural model. Actual area where correlation causes harmful interference could be defined from pilot signal levels difference and processing gain value. In coordinated case wanted pilot signal should be amplified on processing gain value compared to interfering pilot signal from neighbor cell and at the edge of the cell  wanted pilot-to-interfering pilot ratio would be close to 21 dB  (Processing gain= 10∙lg(1250/9.6)=21 dB). Therefore it is proposed to define correlation area as area where  wanted pilot-to-interfering pilot ratio is lower than 21 dB. All radio parameters were taken from cross border study ECC Report 97. The effect of propagation on correlation area percentage is illustrated below. Colorbar provides grade for wanted pilot-to-interfering pilot ratio, interfered areas are colored in blue tones and non-interfered in red and yellow tones.

Figure 6

The calculation results of correlation area percentage with regard to propagation are presented in Annex 2. Because interference could occur inside the network and not only on the edge the criterion used in cross-border study can’t be applied. The separation distance which corresponds to the threshold is defined as minimum distance when 1% or less of cell area could be interfered by uncoordinated BS.

The analisys in Annex 2 showed that interfered area become lower than 1% with the separation distance between 40 and 42 km. In more detailed analysis it was found that 41 km almost exactly corresponds to 1% of correlation area. The cell correlation area variant for 41 km separation distance is presented below.

Figure 7

For this distance the threshold level is defined using SEAMCAT, the exact way it was defined in ECC Report 97. To provide permitted level on the boreder 25 kHz band receiver on a height of 3 meters was modeled in SEAMCAT 3 on a distance of 20.5 km from the closest BS in CDMA cluster. The modeled case and the correspond level -107.5 dBm shown on the figure below. Yellow point denotes measuring receiver location on the border and red points denote interfering CDMA BS cluster, blue point have no physical meaning for the study and just obligatory for SEAMCAT simulation.

Figure 8

This level is 3.5 dB less than level received for coordinated case and proposed to be used as a maximum permitted level for uncoordinated networks. The calculation of relevant field strength level for uncoordinated networks case in 450 MHz band is presented below:

| Central frequency of downlink band | Threshold field strength level on the border (rounded)* | Overall CDMA BS signal strength on the border** |
| --- | --- | --- |
| 465 MHz | 23 dBuV/m/ 25 kHz | 40 dBuV/m/ 1.25 MHz |

Table 2

* - measured in a bandwidth of 25 kHz at a height of 3 metres in 50% of time.

**- measured in a bandwidth of 1250 kHz at a height of 3 metres in 50% of time (recommended)

# conclusions

To provide maximum coverage in border areas where concerned Administration using CDMA systems based on CDMA2000 interface with coincident frequency plans to prevent mutual harmful interference it is strongly recommended to use code coordination what leads to higher permitted levels of maximum field strength on the border.  The procedure for allocation of preferential and non-preferential codes is provided in this report. 5% or even less of codes should be excluded from border areas to prevent any possibility of correlation between base stations of different Administration.

The threshold level 43.5 dBuV/m is proposed for the case of two coordinated CDMA networks in 450 band using aligned frequencies and preferential codes. For uncoordinated networks and when there is no exact information about CDMA networks frequency plans the level of 40 dBuV/m is proposed. If the network operators on both sides of the border are prepared to accept higher levels of interference than the coordinated level to work closer to the borders with some impact on the loss of service it is even more important to perform code coordination to prevent higher probability of correlation between neighboring networks signals.

# BIBLIOGRAPHY

[1]	ECC Report 97 “Cross Border Interference for Land Mobile Technologies”

[2]	ERC Recommendation T/R 25-08 “Planning Criteria and Coordination of Frequencies in the Land Mobile Service in the Range 29.7-921 MHz”

[3]	ERC Recommendation 01-01 “Border Coordination of UMTS/IMT-2000 Systems”.

[4]	3GPP2 C.S0002-C “Physical Layer Standard for cdma2000 Spread Spectrum Systems”

# ANNEX 1: Tables with correlation area percentage (geometrical approach)

Separation distance 12 km

|  | v1 | zone | v2 | zone | v3 | zone | v4 | zone | v5 | zone | v6 | zone | v7 | zone | v8 | zone | v9 | zone | v10 | zone | v11 | zone | v12 | zone | v13 | zone | v14 | zone | v15 | zone | v16 | zone | v17 | zone | v18 | zone | v19 | zone |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 0,0 | 0,0 | 10,4 | 1,0 | 1,3 | 1,0 | 1,7 | 1,0 | 1,7 | 1,0 | 0,8 | 1,0 | 2,8 | 2,0 | 8,8 | 2,0 | 8,8 | 2,0 | 8,8 | 2,0 | 1,9 | 2,0 | 0,4 | 2,0 | 1,4 | 2,0 | 1,4 | 2,0 | 0,9 | 2,0 | 0,9 | 2,0 | 4,5 | 3,0 | 2,8 | 3,0 | 1,9 | 3,0 |
| i2 | 10,4 | 1,0 | 10,4 | 1,0 | 10,4 | 1,0 | 0,8 | 1,0 | 1,7 | 1,0 | 1,7 | 1,0 | 0,8 | 1,0 | 1,9 | 2,0 | 8,8 | 2,0 | 8,8 | 2,0 | 8,8 | 2,0 | 1,9 | 2,0 | 0,9 | 2,0 | 1,4 | 2,0 | 1,4 | 2,0 | 0,9 | 2,0 | 2,8 | 3,0 | 4,5 | 3,0 | 2,8 | 3,0 |
| i3 | 1,3 | 1,0 | 10,4 | 1,0 | 10,4 | 1,0 | 2,8 | 2,0 | 0,8 | 1,0 | 1,7 | 1,0 | 1,7 | 1,0 | 0,4 | 2,0 | 1,9 | 2,0 | 8,8 | 2,0 | 8,8 | 2,0 | 8,8 | 2,0 | 8,8 | 2,0 | 0,9 | 2,0 | 1,4 | 2,0 | 1,4 | 2,0 | 1,9 | 3,0 | 2,8 | 3,0 | 4,5 | 3,0 |
| i4 | 1,7 | 1,0 | 0,8 | 1,0 | 2,8 | 2,0 | 2,8 | 2,0 | 8,8 | 2,0 | 1,9 | 2,0 | 0,4 | 2,0 | 1,4 | 2,0 | 1,4 | 2,0 | 0,9 | 2,0 | 0,9 | 2,0 | 1,7 | 3,0 | 4,5 | 3,0 | 2,8 | 3,0 | 1,9 | 3,0 | 1,1 | 3,0 | 1,0 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i5 | 1,7 | 1,0 | 1,7 | 1,0 | 0,8 | 1,0 | 8,8 | 2,0 | 8,8 | 2,0 | 8,8 | 2,0 | 1,9 | 2,0 | 0,9 | 2,0 | 1,4 | 2,0 | 1,4 | 2,0 | 0,9 | 2,0 | 0,9 | 2,0 | 2,8 | 3,0 | 4,5 | 3,0 | 2,8 | 3,0 | 1,9 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 0,4 | 3,0 |
| i6 | 0,8 | 1,0 | 1,7 | 1,0 | 1,7 | 1,0 | 1,9 | 2,0 | 8,8 | 2,0 | 8,8 | 2,0 | 8,8 | 2,0 | 8,8 | 2,0 | 0,9 | 2,0 | 1,4 | 2,0 | 1,4 | 2,0 | 0,9 | 2,0 | 1,9 | 3,0 | 2,8 | 3,0 | 4,5 | 3,0 | 2,8 | 3,0 | 0,4 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i7 | 2,8 | 2,0 | 0,8 | 1,0 | 1,7 | 1,0 | 0,4 | 2,0 | 1,9 | 2,0 | 8,8 | 2,0 | 8,8 | 2,0 | 1,7 | 3,0 | 1,7 | 3,0 | 0,9 | 2,0 | 1,4 | 2,0 | 1,4 | 2,0 | 1,1 | 3,0 | 1,9 | 3,0 | 2,8 | 3,0 | 4,5 | 3,0 | 4,5 | 3,0 | 0,4 | 3,0 | 1,0 | 3,0 |
| i8 | 8,8 | 2,0 | 1,9 | 2,0 | 0,4 | 2,0 | 1,4 | 2,0 | 0,9 | 2,0 | 0,9 | 2,0 | 1,7 | 3,0 | 4,5 | 3,0 | 2,8 | 3,0 | 1,9 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,0 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i9 | 0,0 | 0,0 | 8,8 | 2,0 | 1,9 | 2,0 | 1,4 | 2,0 | 1,4 | 2,0 | 0,9 | 2,0 | 0,9 | 2,0 | 2,8 | 3,0 | 4,5 | 3,0 | 2,8 | 3,0 | 1,9 | 3,0 | 1,1 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i10 | 8,8 | 2,0 | 8,8 | 2,0 | 8,8 | 2,0 | 0,9 | 2,0 | 1,4 | 2,0 | 1,4 | 2,0 | 0,9 | 2,0 | 1,9 | 3,0 | 2,8 | 3,0 | 4,5 | 3,0 | 2,8 | 3,0 | 1,9 | 3,0 | 0,4 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i11 | 1,9 | 2,0 | 8,8 | 2,0 | 8,8 | 2,0 | 8,8 | 2,0 | 0,9 | 2,0 | 1,4 | 2,0 | 1,4 | 2,0 | 1,1 | 3,0 | 1,9 | 3,0 | 2,8 | 3,0 | 4,5 | 3,0 | 2,8 | 3,0 | 2,8 | 3,0 | 0,4 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i12 | 0,4 | 2,0 | 1,9 | 2,0 | 8,8 | 2,0 | 1,7 | 3,0 | 1,7 | 3,0 | 0,9 | 2,0 | 1,4 | 2,0 | 1,4 | 2,0 | 1,1 | 3,0 | 1,9 | 3,0 | 2,8 | 3,0 | 4,5 | 3,0 | 4,5 | 3,0 | 4,5 | 3,0 | 0,4 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i13 | 1,4 | 2,0 | 0,9 | 2,0 | 0,9 | 2,0 | 4,5 | 3,0 | 2,8 | 3,0 | 1,9 | 3,0 | 1,1 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i14 | 1,4 | 2,0 | 1,4 | 2,0 | 0,9 | 2,0 | 2,8 | 3,0 | 4,5 | 3,0 | 2,8 | 3,0 | 1,9 | 3,0 | 0,4 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i15 | 0,9 | 2,0 | 1,4 | 2,0 | 1,4 | 2,0 | 1,9 | 3,0 | 2,8 | 3,0 | 4,5 | 3,0 | 2,8 | 3,0 | 2,8 | 3,0 | 0,4 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i16 | 0,0 | 0,0 | 0,9 | 2,0 | 1,4 | 2,0 | 1,1 | 3,0 | 1,9 | 3,0 | 2,8 | 3,0 | 4,5 | 3,0 | 4,5 | 3,0 | 4,5 | 3,0 | 0,4 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i17 | 4,5 | 3,0 | 2,8 | 3,0 | 1,9 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i18 | 2,8 | 3,0 | 4,5 | 3,0 | 2,8 | 3,0 | 0,4 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i19 | 1,9 | 3,0 | 2,8 | 3,0 | 4,5 | 3,0 | 4,5 | 3,0 | 0,4 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |

Separation distance 14 km

|  | v1 | zone | v2 | zone | v3 | zone | v4 | zone | v5 | zone | v6 | zone | v7 | zone | v8 | zone | v9 | zone | v10 | zone | v11 | zone | v12 | zone | v13 | zone | v14 | zone | v15 | zone | v16 | zone | v17 | zone | v18 | zone | v19 | zone |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 1,9 | 3,0 | 2,8 | 1,0 | 1,1 | 1,0 | 1,4 | 1,0 | 1,4 | 1,0 | 0,0 | 1,0 | 2,2 | 2,0 | 2,6 | 2,0 | 4,9 | 2,0 | 2,6 | 2,0 | 1,6 | 2,0 | 1,6 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 3,3 | 3,0 | 2,4 | 3,0 | 2,1 | 3,0 | 1,6 | 3,0 |
| i2 | 2,8 | 1,0 | 2,8 | 1,0 | 2,8 | 1,0 | 0,0 | 1,0 | 1,4 | 1,0 | 1,4 | 1,0 | 0,0 | 1,0 | 1,6 | 2,0 | 2,6 | 2,0 | 4,9 | 2,0 | 2,6 | 2,0 | 1,6 | 2,0 | 1,6 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 2,1 | 3,0 | 2,4 | 3,0 | 2,1 | 3,0 |
| i3 | 1,1 | 1,0 | 2,8 | 1,0 | 2,8 | 1,0 | 2,2 | 2,0 | 0,0 | 1,0 | 1,4 | 1,0 | 1,4 | 1,0 | 1,4 | 1,0 | 1,6 | 2,0 | 2,6 | 2,0 | 4,9 | 2,0 | 2,6 | 2,0 | 3,3 | 3,0 | 3,3 | 3,0 | 1,0 | 2,0 | 1,0 | 2,0 | 1,6 | 3,0 | 2,1 | 3,0 | 2,4 | 3,0 |
| i4 | 1,4 | 1,0 | 0,0 | 1,0 | 2,2 | 2,0 | 4,9 | 2,0 | 2,6 | 2,0 | 1,6 | 2,0 | 1,6 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 3,3 | 3,0 | 1,5 | 3,0 | 2,4 | 3,0 | 2,1 | 3,0 | 1,6 | 3,0 | 0,5 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 |
| i5 | 1,4 | 1,0 | 1,4 | 1,0 | 0,0 | 1,0 | 2,6 | 2,0 | 4,9 | 2,0 | 2,6 | 2,0 | 1,6 | 2,0 | 1,6 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 3,3 | 3,0 | 2,1 | 3,0 | 2,4 | 3,0 | 2,1 | 3,0 | 1,6 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 |
| i6 | 0,0 | 1,0 | 1,4 | 1,0 | 1,4 | 1,0 | 1,6 | 2,0 | 2,6 | 2,0 | 4,9 | 2,0 | 2,6 | 2,0 | 3,3 | 3,0 | 3,3 | 3,0 | 1,0 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 1,6 | 3,0 | 2,1 | 3,0 | 2,4 | 3,0 | 2,1 | 3,0 | 2,1 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 |
| i7 | 2,2 | 2,0 | 0,0 | 1,0 | 1,4 | 1,0 | 1,4 | 1,0 | 1,6 | 2,0 | 2,6 | 2,0 | 4,9 | 2,0 | 1,5 | 3,0 | 3,3 | 3,0 | 3,3 | 3,0 | 1,0 | 2,0 | 1,0 | 2,0 | 0,5 | 3,0 | 1,6 | 3,0 | 2,1 | 3,0 | 2,4 | 3,0 | 2,4 | 3,0 | 2,4 | 3,0 | 0,3 | 3,0 |
| i8 | 2,6 | 2,0 | 1,6 | 2,0 | 1,6 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 3,3 | 3,0 | 1,5 | 3,0 | 2,4 | 3,0 | 2,1 | 3,0 | 1,6 | 3,0 | 0,5 | 3,0 | 0,5 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 |
| i9 | 4,9 | 2,0 | 2,6 | 2,0 | 1,6 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 3,3 | 3,0 | 2,1 | 3,0 | 2,4 | 3,0 | 2,1 | 3,0 | 1,6 | 3,0 | 0,5 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 |
| i10 | 2,6 | 2,0 | 4,9 | 2,0 | 2,6 | 2,0 | 2,6 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 1,6 | 3,0 | 2,1 | 3,0 | 2,4 | 3,0 | 2,1 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 |
| i11 | 1,6 | 2,0 | 2,6 | 2,0 | 4,9 | 2,0 | 3,3 | 3,0 | 3,3 | 3,0 | 1,0 | 2,0 | 1,0 | 2,0 | 0,5 | 3,0 | 1,6 | 3,0 | 2,1 | 3,0 | 2,4 | 3,0 | 2,1 | 3,0 | 2,1 | 3,0 | 2,1 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 |
| i12 | 1,0 | 3,0 | 1,6 | 2,0 | 2,6 | 2,0 | 1,5 | 3,0 | 3,3 | 3,0 | 3,3 | 3,0 | 1,0 | 2,0 | 1,0 | 2,0 | 0,5 | 3,0 | 1,6 | 3,0 | 2,1 | 3,0 | 2,4 | 3,0 | 2,4 | 3,0 | 2,4 | 3,0 | 2,4 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 |
| i13 | 1,0 | 2,0 | 1,0 | 2,0 | 3,3 | 3,0 | 2,4 | 3,0 | 2,1 | 3,0 | 1,6 | 3,0 | 0,5 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 |
| i14 | 1,0 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 2,1 | 3,0 | 2,4 | 3,0 | 2,1 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 |
| i15 | 0,4 | 3,0 | 1,0 | 2,0 | 1,0 | 2,0 | 1,6 | 3,0 | 2,1 | 3,0 | 2,4 | 3,0 | 2,1 | 3,0 | 2,1 | 3,0 | 2,1 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 |
| i16 | 3,3 | 3,0 | 3,3 | 3,0 | 1,0 | 2,0 | 0,5 | 3,0 | 1,6 | 3,0 | 2,1 | 3,0 | 2,4 | 3,0 | 2,4 | 3,0 | 2,4 | 3,0 | 2,4 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 |
| i17 | 2,4 | 3,0 | 2,1 | 3,0 | 1,6 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 |
| i18 | 2,1 | 3,0 | 2,4 | 3,0 | 2,1 | 3,0 | 2,1 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 |
| i19 | 1,6 | 3,0 | 2,1 | 3,0 | 2,4 | 3,0 | 2,4 | 3,0 | 2,4 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 |

Separation distance 16 km

|  | v1 | zone | v2 | zone | v3 | zone | v4 | zone | v5 | zone | v6 | zone | v7 | zone | v8 | zone | v9 | zone | v10 | zone | v11 | zone | v12 | zone | v13 | zone | v14 | zone | v15 | zone | v16 | zone | v17 | zone | v18 | zone | v19 | zone |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 5,6 | 1,0 | 2,2 | 1,0 | 0,8 | 1,0 | 1,0 | 1,0 | 1,0 | 1,0 | 1,0 | 1,0 | 1,9 | 2,0 | 2,0 | 2,0 | 2,4 | 2,0 | 2,0 | 2,0 | 1,3 | 2,0 | 1,3 | 2,0 | 0,3 | 2,0 | 0,3 | 2,0 | 0,3 | 2,0 | 2,3 | 3,0 | 1,9 | 3,0 | 1,8 | 3,0 | 1,3 | 3,0 |
| i2 | 2,2 | 1,0 | 5,6 | 1,0 | 2,2 | 1,0 | 2,2 | 1,0 | 1,0 | 1,0 | 1,0 | 1,0 | 1,0 | 1,0 | 1,3 | 2,0 | 2,0 | 2,0 | 2,4 | 2,0 | 2,0 | 2,0 | 1,3 | 2,0 | 1,3 | 2,0 | 0,3 | 2,0 | 0,3 | 2,0 | 0,3 | 2,0 | 1,8 | 3,0 | 1,9 | 3,0 | 1,8 | 3,0 |
| i3 | 0,8 | 1,0 | 2,2 | 1,0 | 5,6 | 1,0 | 1,9 | 2,0 | 1,9 | 2,0 | 1,0 | 1,0 | 1,0 | 1,0 | 1,0 | 1,0 | 1,3 | 2,0 | 2,0 | 2,0 | 2,4 | 2,0 | 2,0 | 2,0 | 2,3 | 3,0 | 2,3 | 3,0 | 0,3 | 2,0 | 0,3 | 2,0 | 1,3 | 3,0 | 1,8 | 3,0 | 1,9 | 3,0 |
| i4 | 1,0 | 1,0 | 1,0 | 1,0 | 1,9 | 2,0 | 2,4 | 2,0 | 2,0 | 2,0 | 1,3 | 2,0 | 1,3 | 2,0 | 0,3 | 2,0 | 0,3 | 2,0 | 0,3 | 2,0 | 2,3 | 3,0 | 1,2 | 3,0 | 1,9 | 3,0 | 1,8 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 |
| i5 | 1,0 | 1,0 | 1,0 | 1,0 | 1,0 | 1,0 | 2,0 | 2,0 | 2,4 | 2,0 | 2,0 | 2,0 | 1,3 | 2,0 | 1,3 | 2,0 | 0,3 | 2,0 | 0,3 | 2,0 | 0,3 | 2,0 | 2,3 | 3,0 | 1,8 | 3,0 | 1,9 | 3,0 | 1,8 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 |
| i6 | 0,3 | 3,0 | 1,0 | 1,0 | 1,0 | 1,0 | 1,3 | 2,0 | 2,0 | 2,0 | 2,4 | 2,0 | 2,0 | 2,0 | 2,3 | 3,0 | 2,3 | 3,0 | 0,3 | 2,0 | 0,3 | 2,0 | 0,3 | 2,0 | 1,3 | 3,0 | 1,8 | 3,0 | 1,9 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 |
| i7 | 1,9 | 2,0 | 1,9 | 2,0 | 1,0 | 1,0 | 1,0 | 1,0 | 1,3 | 2,0 | 2,0 | 2,0 | 2,4 | 2,0 | 1,2 | 3,0 | 2,3 | 3,0 | 2,3 | 3,0 | 0,3 | 2,0 | 0,3 | 2,0 | 0,3 | 2,0 | 1,3 | 3,0 | 1,8 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 |
| i8 | 2,0 | 2,0 | 1,3 | 2,0 | 1,3 | 2,0 | 0,3 | 2,0 | 0,3 | 2,0 | 2,3 | 3,0 | 1,2 | 3,0 | 1,9 | 3,0 | 1,8 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 |
| i9 | 2,4 | 2,0 | 2,0 | 2,0 | 1,3 | 2,0 | 0,3 | 2,0 | 0,3 | 2,0 | 0,3 | 2,0 | 2,3 | 3,0 | 1,8 | 3,0 | 1,9 | 3,0 | 1,8 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 |
| i10 | 2,0 | 2,0 | 2,4 | 2,0 | 2,0 | 2,0 | 2,0 | 2,0 | 0,3 | 2,0 | 0,3 | 2,0 | 0,3 | 2,0 | 1,3 | 3,0 | 1,8 | 3,0 | 1,9 | 3,0 | 1,8 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 |
| i11 | 1,3 | 2,0 | 2,0 | 2,0 | 2,4 | 2,0 | 2,3 | 3,0 | 2,3 | 3,0 | 0,3 | 2,0 | 0,3 | 2,0 | 0,3 | 2,0 | 1,3 | 3,0 | 1,8 | 3,0 | 1,9 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 |
| i12 | 0,3 | 3,0 | 1,3 | 2,0 | 2,0 | 2,0 | 1,2 | 3,0 | 2,3 | 3,0 | 2,3 | 3,0 | 0,3 | 2,0 | 0,3 | 2,0 | 0,3 | 2,0 | 1,3 | 3,0 | 1,8 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 |
| i13 | 0,3 | 2,0 | 0,3 | 2,0 | 2,3 | 3,0 | 1,9 | 3,0 | 1,8 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 |
| i14 | 0,3 | 2,0 | 0,3 | 2,0 | 0,3 | 2,0 | 1,8 | 3,0 | 1,9 | 3,0 | 1,8 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 |
| i15 | 0,3 | 3,0 | 0,3 | 2,0 | 0,3 | 2,0 | 1,3 | 3,0 | 1,8 | 3,0 | 1,9 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 |
| i16 | 2,3 | 3,0 | 2,3 | 3,0 | 0,3 | 2,0 | 0,3 | 2,0 | 1,3 | 3,0 | 1,8 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 |
| i17 | 1,9 | 3,0 | 1,8 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 |
| i18 | 1,8 | 3,0 | 1,9 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 |
| i19 | 1,3 | 3,0 | 1,8 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 | 1,9 | 3,0 |

Separation distance 18 km

|  | v1 | zone | v2 | zone | v3 | zone | v4 | zone | v5 | zone | v6 | zone | v7 | zone | v8 | zone | v9 | zone | v10 | zone | v11 | zone | v12 | zone | v13 | zone | v14 | zone | v15 | zone | v16 | zone | v17 | zone | v18 | zone | v19 | zone |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 2,5 | 1,0 | 1,8 | 1,0 | 0,3 | 1,0 | 0,2 | 1,0 | 0,2 | 1,0 | 0,2 | 1,0 | 1,7 | 2,0 | 1,7 | 2,0 | 1,9 | 2,0 | 1,7 | 2,0 | 1,0 | 2,0 | 7,9 | 3,0 | 7,9 | 3,0 | 7,9 | 3,0 | 6,7 | 3,0 | 1,9 | 3,0 | 1,6 | 3,0 | 1,4 | 3,0 | 0,9 | 3,0 |
| i2 | 1,8 | 1,0 | 2,5 | 1,0 | 1,8 | 1,0 | 1,8 | 1,0 | 0,2 | 1,0 | 0,2 | 1,0 | 0,2 | 1,0 | 1,0 | 2,0 | 1,7 | 2,0 | 1,9 | 2,0 | 1,7 | 2,0 | 1,0 | 2,0 | 6,7 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 1,4 | 3,0 | 1,6 | 3,0 | 1,4 | 3,0 |
| i3 | 0,3 | 1,0 | 1,8 | 1,0 | 2,5 | 1,0 | 1,7 | 2,0 | 1,7 | 2,0 | 0,2 | 1,0 | 0,2 | 1,0 | 7,9 | 3,0 | 1,0 | 2,0 | 1,7 | 2,0 | 1,9 | 2,0 | 1,7 | 2,0 | 1,9 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 0,9 | 3,0 | 1,4 | 3,0 | 1,6 | 3,0 |
| i4 | 0,2 | 1,0 | 0,2 | 1,0 | 1,7 | 2,0 | 1,9 | 2,0 | 1,7 | 2,0 | 1,0 | 2,0 | 7,9 | 3,0 | 7,9 | 3,0 | 7,9 | 3,0 | 6,7 | 3,0 | 1,9 | 3,0 | 0,9 | 3,0 | 1,6 | 3,0 | 1,4 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i5 | 0,2 | 1,0 | 0,2 | 1,0 | 0,2 | 1,0 | 1,7 | 2,0 | 1,9 | 2,0 | 1,7 | 2,0 | 1,0 | 2,0 | 6,7 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 1,9 | 3,0 | 1,4 | 3,0 | 1,6 | 3,0 | 1,4 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i6 | 1,8 | 3,0 | 0,2 | 1,0 | 0,2 | 1,0 | 1,0 | 2,0 | 1,7 | 2,0 | 1,9 | 2,0 | 1,7 | 2,0 | 1,9 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 0,9 | 3,0 | 1,4 | 3,0 | 1,6 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 |
| i7 | 1,7 | 2,0 | 1,7 | 2,0 | 0,2 | 1,0 | 7,9 | 3,0 | 1,0 | 2,0 | 1,7 | 2,0 | 1,9 | 2,0 | 0,9 | 3,0 | 1,9 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 0,9 | 3,0 | 1,4 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 |
| i8 | 1,7 | 2,0 | 1,0 | 2,0 | 7,9 | 3,0 | 7,9 | 3,0 | 6,7 | 3,0 | 1,9 | 3,0 | 0,9 | 3,0 | 1,6 | 3,0 | 1,4 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i9 | 1,9 | 2,0 | 1,7 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 6,7 | 3,0 | 1,9 | 3,0 | 1,4 | 3,0 | 1,6 | 3,0 | 1,4 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i10 | 1,7 | 2,0 | 1,9 | 2,0 | 1,7 | 2,0 | 6,7 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 0,9 | 3,0 | 1,4 | 3,0 | 1,6 | 3,0 | 1,4 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i11 | 1,0 | 2,0 | 1,7 | 2,0 | 1,9 | 2,0 | 1,9 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 0,9 | 3,0 | 1,4 | 3,0 | 1,6 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 |
| i12 | 7,9 | 3,0 | 1,0 | 2,0 | 1,7 | 2,0 | 0,9 | 3,0 | 1,9 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 0,9 | 3,0 | 1,4 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 |
| i13 | 1,3 | 3,0 | 6,7 | 3,0 | 1,9 | 3,0 | 1,6 | 3,0 | 1,4 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i14 | 1,3 | 3,0 | 1,3 | 3,0 | 6,7 | 3,0 | 1,4 | 3,0 | 1,6 | 3,0 | 1,4 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i15 | 6,7 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 0,9 | 3,0 | 1,4 | 3,0 | 1,6 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 |
| i16 | 1,9 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 6,7 | 3,0 | 0,9 | 3,0 | 1,4 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 |
| i17 | 1,6 | 3,0 | 1,4 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i18 | 1,4 | 3,0 | 1,6 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 |
| i19 | 0,9 | 3,0 | 1,4 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 |

Separation distance 20 km

|  | v1 | zone | v2 | zone | v3 | zone | v4 | zone | v5 | zone | v6 | zone | v7 | zone | v8 | zone | v9 | zone | v10 | zone | v11 | zone | v12 | zone | v13 | zone | v14 | zone | v15 | zone | v16 | zone | v17 | zone | v18 | zone | v19 | zone |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 1,9 | 1,0 | 1,5 | 1,0 | 1,5 | 1,0 | 1,5 | 1,0 | 1,5 | 1,0 | 3,0 | 2,0 | 1,5 | 2,0 | 1,4 | 2,0 | 1,6 | 2,0 | 1,4 | 2,0 | 0,3 | 2,0 | 2,8 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 2,5 | 3,0 | 1,6 | 3,0 | 1,3 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 |
| i2 | 1,5 | 1,0 | 1,9 | 1,0 | 1,5 | 1,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 0,3 | 2,0 | 1,4 | 2,0 | 1,6 | 2,0 | 1,4 | 2,0 | 0,3 | 2,0 | 2,5 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 2,5 | 3,0 | 1,1 | 3,0 | 1,3 | 3,0 | 1,1 | 3,0 |
| i3 | 1,6 | 3,0 | 1,5 | 1,0 | 1,9 | 1,0 | 1,5 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 2,8 | 3,0 | 0,3 | 2,0 | 1,4 | 2,0 | 1,6 | 2,0 | 1,4 | 2,0 | 1,6 | 3,0 | 2,5 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 1,1 | 3,0 | 1,3 | 3,0 |
| i4 | 0,9 | 3,0 | 3,0 | 2,0 | 1,5 | 2,0 | 1,6 | 2,0 | 1,4 | 2,0 | 0,3 | 2,0 | 2,8 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 2,5 | 3,0 | 1,6 | 3,0 | 0,1 | 3,0 | 1,3 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 |
| i5 | 0,9 | 3,0 | 0,9 | 3,0 | 3,0 | 2,0 | 1,4 | 2,0 | 1,6 | 2,0 | 1,4 | 2,0 | 0,3 | 2,0 | 2,5 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 2,5 | 3,0 | 1,6 | 3,0 | 1,1 | 3,0 | 1,3 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 |
| i6 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 0,3 | 2,0 | 1,4 | 2,0 | 1,6 | 2,0 | 1,4 | 2,0 | 1,6 | 3,0 | 2,5 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 2,5 | 3,0 | 2,5 | 3,0 | 1,1 | 3,0 | 1,3 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 |
| i7 | 1,5 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 2,8 | 3,0 | 0,3 | 2,0 | 1,4 | 2,0 | 1,6 | 2,0 | 0,1 | 3,0 | 1,6 | 3,0 | 2,5 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 1,1 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 |
| i8 | 1,4 | 2,0 | 0,3 | 2,0 | 2,8 | 3,0 | 7,0 | 3,0 | 2,5 | 3,0 | 1,6 | 3,0 | 0,1 | 3,0 | 1,3 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 |
| i9 | 1,6 | 2,0 | 1,4 | 2,0 | 0,3 | 2,0 | 7,0 | 3,0 | 7,0 | 3,0 | 2,5 | 3,0 | 1,6 | 3,0 | 1,1 | 3,0 | 1,3 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 |
| i10 | 1,4 | 2,0 | 1,6 | 2,0 | 1,4 | 2,0 | 2,5 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 2,5 | 3,0 | 2,5 | 3,0 | 1,1 | 3,0 | 1,3 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 |
| i11 | 0,3 | 2,0 | 1,4 | 2,0 | 1,6 | 2,0 | 1,6 | 3,0 | 2,5 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 1,1 | 3,0 | 1,3 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 |
| i12 | 2,8 | 3,0 | 0,3 | 2,0 | 1,4 | 2,0 | 0,1 | 3,0 | 1,6 | 3,0 | 2,5 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 1,1 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 |
| i13 | 7,0 | 3,0 | 2,5 | 3,0 | 1,6 | 3,0 | 1,3 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 |
| i14 | 7,0 | 3,0 | 7,0 | 3,0 | 2,5 | 3,0 | 1,1 | 3,0 | 1,3 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 |
| i15 | 2,5 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 1,1 | 3,0 | 1,3 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 |
| i16 | 1,6 | 3,0 | 2,5 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 1,1 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 |
| i17 | 1,3 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 |
| i18 | 1,1 | 3,0 | 1,3 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 | 1,1 | 3,0 |
| i19 | 1,6 | 3,0 | 1,1 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 |

Separation distance 22 km

|  | v1 | zone | v2 | zone | v3 | zone | v4 | zone | v5 | zone | v6 | zone | v7 | zone | v8 | zone | v9 | zone | v10 | zone | v11 | zone | v12 | zone | v13 | zone | v14 | zone | v15 | zone | v16 | zone | v17 | zone | v18 | zone | v19 | zone |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 1,6 | 1,0 | 1,2 | 1,0 | 1,2 | 1,0 | 9,8 | 2,0 | 9,8 | 2,0 | 2,2 | 2,0 | 1,2 | 2,0 | 1,0 | 2,0 | 1,3 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 2,2 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 2,0 | 3,0 | 1,3 | 3,0 | 0,8 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i2 | 1,2 | 1,0 | 1,6 | 1,0 | 1,2 | 1,0 | 2,2 | 2,0 | 9,8 | 2,0 | 9,8 | 2,0 | 2,2 | 2,0 | 2,2 | 2,0 | 1,0 | 2,0 | 1,3 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 2,0 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 2,0 | 3,0 | 0,4 | 3,0 | 0,8 | 3,0 | 0,4 | 3,0 |
| i3 | 1,3 | 3,0 | 1,2 | 1,0 | 1,6 | 1,0 | 1,2 | 2,0 | 2,2 | 2,0 | 9,8 | 2,0 | 9,8 | 2,0 | 2,2 | 3,0 | 2,2 | 3,0 | 1,0 | 2,0 | 1,3 | 2,0 | 1,0 | 2,0 | 1,3 | 3,0 | 2,0 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 0,4 | 3,0 | 0,8 | 3,0 |
| i4 | 9,8 | 2,0 | 2,2 | 2,0 | 1,2 | 2,0 | 1,3 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 2,2 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 2,0 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 0,8 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i5 | 9,8 | 2,0 | 9,8 | 2,0 | 2,2 | 2,0 | 1,0 | 2,0 | 1,3 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 2,0 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 2,0 | 3,0 | 1,3 | 3,0 | 0,4 | 3,0 | 0,8 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i6 | 2,2 | 2,0 | 9,8 | 2,0 | 9,8 | 2,0 | 9,8 | 2,0 | 1,0 | 2,0 | 1,3 | 2,0 | 1,0 | 2,0 | 1,3 | 3,0 | 2,0 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 0,4 | 3,0 | 0,8 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i7 | 1,2 | 2,0 | 2,2 | 2,0 | 9,8 | 2,0 | 2,2 | 3,0 | 2,2 | 3,0 | 1,0 | 2,0 | 1,3 | 2,0 | 1,3 | 2,0 | 1,3 | 3,0 | 2,0 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 0,4 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |
| i8 | 1,0 | 2,0 | 1,0 | 2,0 | 2,2 | 3,0 | 2,6 | 3,0 | 2,0 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 0,8 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i9 | 1,3 | 2,0 | 1,0 | 2,0 | 1,0 | 2,0 | 2,6 | 3,0 | 2,6 | 3,0 | 2,0 | 3,0 | 1,3 | 3,0 | 0,4 | 3,0 | 0,8 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i10 | 1,0 | 2,0 | 1,3 | 2,0 | 1,0 | 2,0 | 2,0 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 0,4 | 3,0 | 0,8 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i11 | 1,1 | 3,0 | 1,0 | 2,0 | 1,3 | 2,0 | 1,3 | 3,0 | 2,0 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 0,4 | 3,0 | 0,8 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i12 | 2,2 | 3,0 | 2,2 | 3,0 | 1,0 | 2,0 | 1,0 | 2,0 | 1,3 | 3,0 | 2,0 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 0,4 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |
| i13 | 2,6 | 3,0 | 2,0 | 3,0 | 1,3 | 3,0 | 0,8 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i14 | 2,6 | 3,0 | 2,6 | 3,0 | 2,0 | 3,0 | 0,4 | 3,0 | 0,8 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i15 | 2,0 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 0,4 | 3,0 | 0,8 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i16 | 1,3 | 3,0 | 2,0 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 0,4 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |
| i17 | 0,8 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i18 | 0,4 | 3,0 | 0,8 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i19 | 1,3 | 3,0 | 0,4 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |

Separation distance 24 km

|  | v1 | zone | v2 | zone | v3 | zone | v4 | zone | v5 | zone | v6 | zone | v7 | zone | v8 | zone | v9 | zone | v10 | zone | v11 | zone | v12 | zone | v13 | zone | v14 | zone | v15 | zone | v16 | zone | v17 | zone | v18 | zone | v19 | zone |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 1,2 | 1,0 | 0,8 | 1,0 | 6,3 | 2,0 | 2,6 | 2,0 | 2,6 | 2,0 | 1,9 | 2,0 | 0,8 | 2,0 | 0,2 | 2,0 | 0,8 | 2,0 | 0,2 | 2,0 | 0,2 | 2,0 | 1,9 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 1,7 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i2 | 0,8 | 1,0 | 1,2 | 1,0 | 0,8 | 1,0 | 1,9 | 2,0 | 2,6 | 2,0 | 2,6 | 2,0 | 1,9 | 2,0 | 1,9 | 2,0 | 0,2 | 2,0 | 0,8 | 2,0 | 0,2 | 2,0 | 0,2 | 2,0 | 1,7 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 |
| i3 | 6,3 | 2,0 | 0,8 | 1,0 | 1,2 | 1,0 | 0,8 | 2,0 | 1,9 | 2,0 | 2,6 | 2,0 | 2,6 | 2,0 | 1,9 | 3,0 | 1,9 | 3,0 | 0,2 | 2,0 | 0,8 | 2,0 | 0,2 | 2,0 | 1,0 | 3,0 | 1,7 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 |
| i4 | 2,6 | 2,0 | 1,9 | 2,0 | 0,8 | 2,0 | 0,8 | 2,0 | 0,2 | 2,0 | 0,2 | 2,0 | 1,9 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 1,7 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i5 | 2,6 | 2,0 | 2,6 | 2,0 | 1,9 | 2,0 | 0,2 | 2,0 | 0,8 | 2,0 | 0,2 | 2,0 | 0,2 | 2,0 | 1,7 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 1,7 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i6 | 1,9 | 2,0 | 2,6 | 2,0 | 2,6 | 2,0 | 2,6 | 2,0 | 0,2 | 2,0 | 0,8 | 2,0 | 0,2 | 2,0 | 1,0 | 3,0 | 1,7 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 |
| i7 | 0,8 | 2,0 | 1,9 | 2,0 | 2,6 | 2,0 | 1,9 | 3,0 | 1,9 | 3,0 | 0,2 | 2,0 | 0,8 | 2,0 | 0,8 | 2,0 | 1,0 | 3,0 | 1,7 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 |
| i8 | 0,2 | 2,0 | 0,2 | 2,0 | 1,9 | 3,0 | 2,0 | 3,0 | 1,7 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i9 | 0,8 | 2,0 | 0,2 | 2,0 | 0,2 | 2,0 | 2,0 | 3,0 | 2,0 | 3,0 | 1,7 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i10 | 0,2 | 2,0 | 0,8 | 2,0 | 0,2 | 2,0 | 1,7 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 |
| i11 | 0,4 | 3,0 | 0,2 | 2,0 | 0,8 | 2,0 | 1,0 | 3,0 | 1,7 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 |
| i12 | 1,9 | 3,0 | 1,9 | 3,0 | 0,2 | 2,0 | 0,2 | 2,0 | 1,0 | 3,0 | 1,7 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 |
| i13 | 2,0 | 3,0 | 1,7 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i14 | 2,0 | 3,0 | 2,0 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 |
| i15 | 1,7 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 |
| i16 | 1,0 | 3,0 | 1,7 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 |
| i17 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i18 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i19 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |

Separation distance 26 km

|  | v1 | zone | v2 | zone | v3 | zone | v4 | zone | v5 | zone | v6 | zone | v7 | zone | v8 | zone | v9 | zone | v10 | zone | v11 | zone | v12 | zone | v13 | zone | v14 | zone | v15 | zone | v16 | zone | v17 | zone | v18 | zone | v19 | zone |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 0,8 | 1,0 | 0,8 | 1,0 | 2,7 | 2,0 | 2,0 | 2,0 | 2,0 | 2,0 | 1,5 | 2,0 | 1,5 | 2,0 | 1,5 | 2,0 | 1,5 | 2,0 | 1,5 | 2,0 | 3,0 | 3,0 | 1,6 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,4 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 |
| i2 | 1,7 | 3,0 | 0,8 | 1,0 | 0,8 | 1,0 | 1,5 | 2,0 | 2,0 | 2,0 | 2,0 | 2,0 | 1,5 | 2,0 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 1,4 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 |
| i3 | 2,7 | 2,0 | 2,7 | 2,0 | 0,8 | 1,0 | 0,8 | 1,0 | 1,5 | 2,0 | 2,0 | 2,0 | 2,0 | 2,0 | 1,6 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 0,3 | 3,0 | 1,4 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 |
| i4 | 2,0 | 2,0 | 1,5 | 2,0 | 1,5 | 2,0 | 1,5 | 2,0 | 1,5 | 2,0 | 3,0 | 3,0 | 1,6 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,4 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 |
| i5 | 2,0 | 2,0 | 2,0 | 2,0 | 1,5 | 2,0 | 1,5 | 2,0 | 1,5 | 2,0 | 1,5 | 2,0 | 3,0 | 3,0 | 1,4 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,4 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 |
| i6 | 1,5 | 2,0 | 2,0 | 2,0 | 2,0 | 2,0 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 0,3 | 3,0 | 1,4 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 |
| i7 | 2,0 | 3,0 | 1,5 | 2,0 | 2,0 | 2,0 | 1,6 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 0,3 | 3,0 | 1,4 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 |
| i8 | 1,0 | 3,0 | 3,0 | 3,0 | 1,6 | 3,0 | 1,7 | 3,0 | 1,4 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 |
| i9 | 1,0 | 3,0 | 1,0 | 3,0 | 3,0 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,4 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 |
| i10 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,4 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 |
| i11 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 0,3 | 3,0 | 1,4 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 |
| i12 | 1,6 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 3,0 | 0,3 | 3,0 | 1,4 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 |
| i13 | 1,7 | 3,0 | 1,4 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 | 0,3 | 3,0 |
| i14 | 1,7 | 3,0 | 1,7 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 |
| i15 | 1,4 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 |
| i16 | 0,3 | 3,0 | 1,4 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 |
| i17 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i18 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i19 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |

Separation distance 28 km

|  | v1 | zone | v2 | zone | v3 | zone | v4 | zone | v5 | zone | v6 | zone | v7 | zone | v8 | zone | v9 | zone | v10 | zone | v11 | zone | v12 | zone | v13 | zone | v14 | zone | v15 | zone | v16 | zone | v17 | zone | v18 | zone | v19 | zone |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 0,3 | 3,0 | 0,3 | 3,0 | 2,1 | 2,0 | 1,7 | 2,0 | 1,7 | 2,0 | 1,2 | 2,0 | 1,2 | 2,0 | 7,0 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 2,2 | 3,0 | 1,3 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i2 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,2 | 2,0 | 1,7 | 2,0 | 1,7 | 2,0 | 1,2 | 2,0 | 2,2 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 2,2 | 3,0 | 1,0 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i3 | 2,1 | 2,0 | 2,1 | 2,0 | 2,1 | 2,0 | 2,1 | 2,0 | 1,2 | 2,0 | 1,7 | 2,0 | 1,7 | 2,0 | 1,3 | 3,0 | 2,2 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 1,0 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 |
| i4 | 1,7 | 2,0 | 1,2 | 2,0 | 1,2 | 2,0 | 1,2 | 2,0 | 7,0 | 3,0 | 2,2 | 3,0 | 1,3 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i5 | 1,7 | 2,0 | 1,7 | 2,0 | 1,2 | 2,0 | 7,0 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 2,2 | 3,0 | 1,0 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i6 | 1,2 | 2,0 | 1,7 | 2,0 | 1,7 | 2,0 | 2,2 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 1,0 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i7 | 1,7 | 3,0 | 1,2 | 2,0 | 1,7 | 2,0 | 1,3 | 3,0 | 2,2 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 1,0 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 |
| i8 | 7,0 | 3,0 | 2,2 | 3,0 | 1,3 | 3,0 | 1,4 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i9 | 0,3 | 3,0 | 7,0 | 3,0 | 2,2 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i10 | 7,0 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 1,0 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i11 | 2,2 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 1,0 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 |
| i12 | 1,3 | 3,0 | 2,2 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 7,0 | 3,0 | 1,0 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 |
| i13 | 1,4 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i14 | 1,4 | 3,0 | 1,4 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i15 | 1,0 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 |
| i16 | 1,7 | 3,0 | 1,0 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 |
| i17 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i18 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i19 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |

Separation distance 30 km

|  | v1 | zone | v2 | zone | v3 | zone | v4 | zone | v5 | zone | v6 | zone | v7 | zone | v8 | zone | v9 | zone | v10 | zone | v11 | zone | v12 | zone | v13 | zone | v14 | zone | v15 | zone | v16 | zone | v17 | zone | v18 | zone | v19 | zone |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 1,0 | 3,0 | 5,0 | 2,0 | 1,8 | 2,0 | 1,3 | 2,0 | 1,3 | 2,0 | 0,8 | 2,0 | 0,8 | 2,0 | 2,6 | 3,0 | 3,7 | 3,0 | 2,6 | 3,0 | 1,8 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i2 | 5,0 | 2,0 | 5,0 | 2,0 | 5,0 | 2,0 | 0,8 | 2,0 | 1,3 | 2,0 | 1,3 | 2,0 | 0,8 | 2,0 | 1,8 | 3,0 | 2,6 | 3,0 | 3,7 | 3,0 | 2,6 | 3,0 | 1,8 | 3,0 | 0,2 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i3 | 1,8 | 2,0 | 5,0 | 2,0 | 5,0 | 2,0 | 5,0 | 2,0 | 0,8 | 2,0 | 1,3 | 2,0 | 1,3 | 2,0 | 1,0 | 3,0 | 1,8 | 3,0 | 2,6 | 3,0 | 3,7 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 0,2 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i4 | 1,3 | 2,0 | 0,8 | 2,0 | 0,8 | 2,0 | 3,7 | 3,0 | 2,6 | 3,0 | 1,8 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i5 | 1,3 | 2,0 | 1,3 | 2,0 | 0,8 | 2,0 | 2,6 | 3,0 | 3,7 | 3,0 | 2,6 | 3,0 | 1,8 | 3,0 | 0,2 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i6 | 0,8 | 2,0 | 1,3 | 2,0 | 1,3 | 2,0 | 1,8 | 3,0 | 2,6 | 3,0 | 3,7 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 0,2 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i7 | 1,4 | 3,0 | 0,8 | 2,0 | 1,3 | 2,0 | 1,0 | 3,0 | 1,8 | 3,0 | 2,6 | 3,0 | 3,7 | 3,0 | 3,7 | 3,0 | 3,7 | 3,0 | 0,2 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i8 | 2,6 | 3,0 | 1,8 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i9 | 3,7 | 3,0 | 2,6 | 3,0 | 1,8 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i10 | 2,6 | 3,0 | 3,7 | 3,0 | 2,6 | 3,0 | 0,2 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i11 | 1,8 | 3,0 | 2,6 | 3,0 | 3,7 | 3,0 | 3,7 | 3,0 | 0,2 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i12 | 1,0 | 3,0 | 1,8 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 2,6 | 3,0 | 0,2 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i13 | 1,0 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i14 | 1,0 | 3,0 | 1,0 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i15 | 0,2 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i16 | 1,4 | 3,0 | 0,2 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i17 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i18 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i19 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |

Separation distance 32 km

|  | v1 | zone | v2 | zone | v3 | zone | v4 | zone | v5 | zone | v6 | zone | v7 | zone | v8 | zone | v9 | zone | v10 | zone | v11 | zone | v12 | zone | v13 | zone | v14 | zone | v15 | zone | v16 | zone | v17 | zone | v18 | zone | v19 | zone |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 3,9 | 2,0 | 2,5 | 2,0 | 1,5 | 2,0 | 0,9 | 2,0 | 0,9 | 2,0 | 0,9 | 2,0 | 3,1 | 3,0 | 2,0 | 3,0 | 2,3 | 3,0 | 2,0 | 3,0 | 1,6 | 3,0 | 0,4 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i2 | 2,5 | 2,0 | 3,9 | 2,0 | 2,5 | 2,0 | 2,5 | 2,0 | 0,9 | 2,0 | 0,9 | 2,0 | 0,9 | 2,0 | 1,6 | 3,0 | 2,0 | 3,0 | 2,3 | 3,0 | 2,0 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i3 | 1,5 | 2,0 | 2,5 | 2,0 | 3,9 | 2,0 | 3,1 | 3,0 | 3,1 | 3,0 | 0,9 | 2,0 | 0,9 | 2,0 | 0,4 | 3,0 | 1,6 | 3,0 | 2,0 | 3,0 | 2,3 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i4 | 0,9 | 2,0 | 0,9 | 2,0 | 3,1 | 3,0 | 2,3 | 3,0 | 2,0 | 3,0 | 1,6 | 3,0 | 0,4 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i5 | 0,9 | 2,0 | 0,9 | 2,0 | 0,9 | 2,0 | 2,0 | 3,0 | 2,3 | 3,0 | 2,0 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i6 | 0,2 | 3,0 | 0,9 | 2,0 | 0,9 | 2,0 | 1,6 | 3,0 | 2,0 | 3,0 | 2,3 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i7 | 3,1 | 3,0 | 3,1 | 3,0 | 0,9 | 2,0 | 0,4 | 3,0 | 1,6 | 3,0 | 2,0 | 3,0 | 2,3 | 3,0 | 2,3 | 3,0 | 2,3 | 3,0 | 2,3 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i8 | 2,0 | 3,0 | 1,6 | 3,0 | 0,4 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i9 | 2,3 | 3,0 | 2,0 | 3,0 | 1,6 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i10 | 2,0 | 3,0 | 2,3 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i11 | 1,6 | 3,0 | 2,0 | 3,0 | 2,3 | 3,0 | 2,3 | 3,0 | 2,3 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i12 | 0,4 | 3,0 | 1,6 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i13 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i14 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i15 | 1,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i16 | 1,0 | 3,0 | 1,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i17 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i18 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i19 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |

Separation distance 34 km

|  | v1 | zone | v2 | zone | v3 | zone | v4 | zone | v5 | zone | v6 | zone | v7 | zone | v8 | zone | v9 | zone | v10 | zone | v11 | zone | v12 | zone | v13 | zone | v14 | zone | v15 | zone | v16 | zone | v17 | zone | v18 | zone | v19 | zone |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 2,3 | 2,0 | 2,0 | 2,0 | 1,2 | 2,0 | 0,0 | 2,0 | 0,0 | 2,0 | 0,0 | 2,0 | 2,2 | 3,0 | 1,7 | 3,0 | 1,8 | 3,0 | 1,7 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 |
| i2 | 2,0 | 2,0 | 2,3 | 2,0 | 2,0 | 2,0 | 2,0 | 2,0 | 0,0 | 2,0 | 0,0 | 2,0 | 0,0 | 2,0 | 1,2 | 3,0 | 1,7 | 3,0 | 1,8 | 3,0 | 1,7 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 |
| i3 | 1,2 | 2,0 | 2,0 | 2,0 | 2,3 | 2,0 | 2,2 | 3,0 | 2,2 | 3,0 | 0,0 | 2,0 | 0,0 | 2,0 | 0,0 | 2,0 | 1,2 | 3,0 | 1,7 | 3,0 | 1,8 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 |
| i4 | 0,0 | 2,0 | 0,0 | 2,0 | 2,2 | 3,0 | 1,8 | 3,0 | 1,7 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 |
| i5 | 0,0 | 2,0 | 0,0 | 2,0 | 0,0 | 2,0 | 1,7 | 3,0 | 1,8 | 3,0 | 1,7 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 |
| i6 | 0,0 | 3,0 | 0,0 | 2,0 | 0,0 | 2,0 | 1,2 | 3,0 | 1,7 | 3,0 | 1,8 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 |
| i7 | 2,2 | 3,0 | 2,2 | 3,0 | 0,0 | 2,0 | 0,0 | 2,0 | 1,2 | 3,0 | 1,7 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 |
| i8 | 1,7 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 |
| i9 | 1,8 | 3,0 | 1,7 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 |
| i10 | 1,7 | 3,0 | 1,8 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 |
| i11 | 1,2 | 3,0 | 1,7 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 | 1,8 | 3,0 |
| i12 | 0,0 | 3,0 | 1,2 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 | 1,7 | 3,0 |
| i13 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i14 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i15 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i16 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i17 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i18 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i19 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |

Separation distance 36 km

|  | v1 | zone | v2 | zone | v3 | zone | v4 | zone | v5 | zone | v6 | zone | v7 | zone | v8 | zone | v9 | zone | v10 | zone | v11 | zone | v12 | zone | v13 | zone | v14 | zone | v15 | zone | v16 | zone | v17 | zone | v18 | zone | v19 | zone |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 1,9 | 2,0 | 1,6 | 2,0 | 0,9 | 2,0 | 0,9 | 2,0 | 0,9 | 2,0 | 4,5 | 3,0 | 1,9 | 3,0 | 1,4 | 3,0 | 1,6 | 3,0 | 1,4 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |
| i2 | 1,6 | 2,0 | 1,9 | 2,0 | 1,6 | 2,0 | 4,5 | 3,0 | 4,5 | 3,0 | 4,5 | 3,0 | 4,5 | 3,0 | 0,8 | 3,0 | 1,4 | 3,0 | 1,6 | 3,0 | 1,4 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |
| i3 | 0,9 | 2,0 | 1,6 | 2,0 | 1,9 | 2,0 | 1,9 | 3,0 | 4,5 | 3,0 | 4,5 | 3,0 | 4,5 | 3,0 | 4,5 | 3,0 | 0,8 | 3,0 | 1,4 | 3,0 | 1,6 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 |
| i4 | 1,2 | 3,0 | 4,5 | 3,0 | 1,9 | 3,0 | 1,6 | 3,0 | 1,4 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |
| i5 | 1,2 | 3,0 | 1,2 | 3,0 | 4,5 | 3,0 | 1,4 | 3,0 | 1,6 | 3,0 | 1,4 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |
| i6 | 4,5 | 3,0 | 4,5 | 3,0 | 4,5 | 3,0 | 0,8 | 3,0 | 1,4 | 3,0 | 1,6 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 |
| i7 | 1,9 | 3,0 | 4,5 | 3,0 | 4,5 | 3,0 | 4,5 | 3,0 | 0,8 | 3,0 | 1,4 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 |
| i8 | 1,4 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |
| i9 | 1,6 | 3,0 | 1,4 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |
| i10 | 1,4 | 3,0 | 1,6 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 |
| i11 | 0,8 | 3,0 | 1,4 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 |
| i12 | 1,7 | 3,0 | 0,8 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 | 1,4 | 3,0 |
| i13 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i14 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i15 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i16 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i17 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i18 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i19 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |

Separation distance 38 km

|  | v1 | zone | v2 | zone | v3 | zone | v4 | zone | v5 | zone | v6 | zone | v7 | zone | v8 | zone | v9 | zone | v10 | zone | v11 | zone | v12 | zone | v13 | zone | v14 | zone | v15 | zone | v16 | zone | v17 | zone | v18 | zone | v19 | zone |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 1,5 | 2,0 | 1,3 | 2,0 | 0,0 | 2,0 | 6,5 | 3,0 | 6,5 | 3,0 | 2,4 | 3,0 | 1,6 | 3,0 | 1,0 | 3,0 | 1,2 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i2 | 1,3 | 2,0 | 1,5 | 2,0 | 1,3 | 2,0 | 2,4 | 3,0 | 6,5 | 3,0 | 6,5 | 3,0 | 2,4 | 3,0 | 2,4 | 3,0 | 1,0 | 3,0 | 1,2 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i3 | 0,0 | 2,0 | 1,3 | 2,0 | 1,5 | 2,0 | 1,6 | 3,0 | 2,4 | 3,0 | 6,5 | 3,0 | 6,5 | 3,0 | 6,5 | 3,0 | 6,5 | 3,0 | 1,0 | 3,0 | 1,2 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i4 | 6,5 | 3,0 | 2,4 | 3,0 | 1,6 | 3,0 | 1,2 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i5 | 6,5 | 3,0 | 6,5 | 3,0 | 2,4 | 3,0 | 1,0 | 3,0 | 1,2 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i6 | 2,4 | 3,0 | 6,5 | 3,0 | 6,5 | 3,0 | 6,5 | 3,0 | 1,0 | 3,0 | 1,2 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i7 | 1,6 | 3,0 | 2,4 | 3,0 | 6,5 | 3,0 | 6,5 | 3,0 | 6,5 | 3,0 | 1,0 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 |
| i8 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i9 | 1,2 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i10 | 1,0 | 3,0 | 1,2 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i11 | 1,6 | 3,0 | 1,0 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 | 1,2 | 3,0 |
| i12 | 1,4 | 3,0 | 1,4 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 | 1,0 | 3,0 |
| i13 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i14 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i15 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i16 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i17 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i18 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i19 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |

Separation distance 40 km

|  | v1 | zone | v2 | zone | v3 | zone | v4 | zone | v5 | zone | v6 | zone | v7 | zone | v8 | zone | v9 | zone | v10 | zone | v11 | zone | v12 | zone | v13 | zone | v14 | zone | v15 | zone | v16 | zone | v17 | zone | v18 | zone | v19 | zone |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 1,2 | 2,0 | 0,9 | 2,0 | 0,9 | 2,0 | 2,5 | 3,0 | 2,5 | 3,0 | 2,0 | 3,0 | 1,3 | 3,0 | 0,2 | 3,0 | 0,7 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i2 | 0,9 | 2,0 | 1,2 | 2,0 | 0,9 | 2,0 | 2,0 | 3,0 | 2,5 | 3,0 | 2,5 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 0,2 | 3,0 | 0,7 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i3 | 1,0 | 3,0 | 0,9 | 2,0 | 1,2 | 2,0 | 1,3 | 3,0 | 2,0 | 3,0 | 2,5 | 3,0 | 2,5 | 3,0 | 2,5 | 3,0 | 2,5 | 3,0 | 0,2 | 3,0 | 0,7 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i4 | 2,5 | 3,0 | 2,0 | 3,0 | 1,3 | 3,0 | 0,7 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i5 | 2,5 | 3,0 | 2,5 | 3,0 | 2,0 | 3,0 | 0,2 | 3,0 | 0,7 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i6 | 2,0 | 3,0 | 2,5 | 3,0 | 2,5 | 3,0 | 2,5 | 3,0 | 0,2 | 3,0 | 0,7 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i7 | 1,3 | 3,0 | 2,0 | 3,0 | 2,5 | 3,0 | 2,5 | 3,0 | 2,5 | 3,0 | 0,2 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 |
| i8 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i9 | 0,7 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i10 | 0,2 | 3,0 | 0,7 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i11 | 1,2 | 3,0 | 0,2 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 |
| i12 | 1,0 | 3,0 | 1,0 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i13 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i14 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i15 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i16 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i17 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i18 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i19 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |

Separation distance 42 km

|  | v1 | zone | v2 | zone | v3 | zone | v4 | zone | v5 | zone | v6 | zone | v7 | zone | v8 | zone | v9 | zone | v10 | zone | v11 | zone | v12 | zone | v13 | zone | v14 | zone | v15 | zone | v16 | zone | v17 | zone | v18 | zone | v19 | zone |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 0,7 | 2,0 | 0,7 | 2,0 | 0,7 | 2,0 | 2,0 | 3,0 | 2,0 | 3,0 | 1,6 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i2 | 0,2 | 3,0 | 0,7 | 2,0 | 0,7 | 2,0 | 1,6 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 |
| i3 | 0,2 | 3,0 | 0,2 | 3,0 | 0,7 | 2,0 | 0,9 | 3,0 | 1,6 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 |
| i4 | 2,0 | 3,0 | 1,6 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i5 | 2,0 | 3,0 | 2,0 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 |
| i6 | 1,6 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 |
| i7 | 0,9 | 3,0 | 1,6 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 |
| i8 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i9 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i10 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i11 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 |
| i12 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i13 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i14 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i15 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i16 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i17 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i18 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i19 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |

Separation distance 44 km

|  | v1 | zone | v2 | zone | v3 | zone | v4 | zone | v5 | zone | v6 | zone | v7 | zone | v8 | zone | v9 | zone | v10 | zone | v11 | zone | v12 | zone | v13 | zone | v14 | zone | v15 | zone | v16 | zone | v17 | zone | v18 | zone | v19 | zone |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 0,9 | 3,0 | 0,9 | 3,0 | 2,8 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,3 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 |
| i2 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,3 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 |
| i3 | 2,8 | 3,0 | 2,8 | 3,0 | 2,8 | 3,0 | 0,1 | 3,0 | 1,3 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 |
| i4 | 1,6 | 3,0 | 1,3 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 | 0,1 | 3,0 |
| i5 | 1,6 | 3,0 | 1,6 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 |
| i6 | 1,3 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 |
| i7 | 0,1 | 3,0 | 1,3 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 | 1,6 | 3,0 |
| i8 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i9 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i10 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i11 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 |
| i12 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i13 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i14 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i15 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i16 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i17 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i18 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i19 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |

Separation distance 46 km

|  | v1 | zone | v2 | zone | v3 | zone | v4 | zone | v5 | zone | v6 | zone | v7 | zone | v8 | zone | v9 | zone | v10 | zone | v11 | zone | v12 | zone | v13 | zone | v14 | zone | v15 | zone | v16 | zone | v17 | zone | v18 | zone | v19 | zone |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 0,1 | 3,0 | 6,6 | 3,0 | 2,1 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i2 | 6,6 | 3,0 | 6,6 | 3,0 | 6,6 | 3,0 | 0,9 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i3 | 2,1 | 3,0 | 6,6 | 3,0 | 6,6 | 3,0 | 6,6 | 3,0 | 0,9 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 |
| i4 | 1,3 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i5 | 1,3 | 3,0 | 1,3 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i6 | 0,9 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 |
| i7 | 1,6 | 3,0 | 0,9 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 | 1,3 | 3,0 |
| i8 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i9 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i10 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i11 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 |
| i12 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i13 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i14 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i15 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i16 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i17 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i18 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i19 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |

Separation distance 48 km

|  | v1 | zone | v2 | zone | v3 | zone | v4 | zone | v5 | zone | v6 | zone | v7 | zone | v8 | zone | v9 | zone | v10 | zone | v11 | zone | v12 | zone | v13 | zone | v14 | zone | v15 | zone | v16 | zone | v17 | zone | v18 | zone | v19 | zone |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 3,2 | 3,0 | 2,5 | 3,0 | 1,8 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i2 | 2,5 | 3,0 | 3,2 | 3,0 | 2,5 | 3,0 | 2,5 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i3 | 1,8 | 3,0 | 2,5 | 3,0 | 3,2 | 3,0 | 3,2 | 3,0 | 3,2 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i4 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i5 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i6 | 1,3 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i7 | 1,3 | 3,0 | 1,3 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i8 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i9 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i10 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i11 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 |
| i12 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i13 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i14 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i15 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i16 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i17 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i18 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i19 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |

Separation distance 50 km

|  | v1 | zone | v2 | zone | v3 | zone | v4 | zone | v5 | zone | v6 | zone | v7 | zone | v8 | zone | v9 | zone | v10 | zone | v11 | zone | v12 | zone | v13 | zone | v14 | zone | v15 | zone | v16 | zone | v17 | zone | v18 | zone | v19 | zone |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 2,2 | 3,0 | 2,0 | 3,0 | 1,5 | 3,0 | 1,5 | 3,0 | 1,5 | 3,0 | 1,5 | 3,0 | 1,5 | 3,0 | 1,5 | 3,0 | 1,5 | 3,0 | 1,5 | 3,0 | 1,5 | 3,0 | 1,5 | 3,0 | 1,5 | 3,0 | 1,5 | 3,0 | 1,5 | 3,0 | 1,5 | 3,0 | 1,5 | 3,0 | 1,5 | 3,0 | 1,5 | 3,0 |
| i2 | 2,0 | 3,0 | 2,2 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 | 2,0 | 3,0 |
| i3 | 1,5 | 3,0 | 2,0 | 3,0 | 2,2 | 3,0 | 2,2 | 3,0 | 2,2 | 3,0 | 2,2 | 3,0 | 2,2 | 3,0 | 2,2 | 3,0 | 2,2 | 3,0 | 2,2 | 3,0 | 2,2 | 3,0 | 2,2 | 3,0 | 2,2 | 3,0 | 2,2 | 3,0 | 2,2 | 3,0 | 2,2 | 3,0 | 2,2 | 3,0 | 2,2 | 3,0 | 2,2 | 3,0 |
| i4 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i5 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i6 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i7 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 | 0,9 | 3,0 |
| i8 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i9 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i10 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i11 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 | 0,7 | 3,0 |
| i12 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 | 0,2 | 3,0 |
| i13 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i14 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i15 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i16 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 | 0,0 | 3,0 |
| i17 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i18 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 | 0,4 | 3,0 |
| i19 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 | 0,8 | 3,0 |

# ANNEX 2: Tables with correlation area percentage (propogation approach)

Separation distance 12 km

|  | v1 | v2 | v3 | v4 | v5 | v6 | v7 | v8 | v9 | v10 | v11 | v12 | v13 | v14 | v15 | v16 | v17 | v18 | v19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 0,00 | 9,26 | 1,30 | 1,68 | 1,68 | 0,82 | 1,56 | 5,23 | 0,00 | 5,23 | 1,19 | 0,43 | 1,41 | 1,41 | 0,87 | 0,00 | 0,13 | 0,07 | 0,05 |
| i2 | 9,26 | 0,00 | 9,26 | 0,82 | 1,68 | 1,68 | 0,82 | 1,19 | 5,23 | 0,00 | 5,23 | 1,19 | 0,87 | 1,41 | 1,41 | 0,87 | 0,07 | 0,13 | 0,07 |
| i3 | 1,30 | 9,26 | 0,00 | 1,56 | 0,82 | 1,68 | 1,68 | 0,43 | 1,19 | 5,23 | 0,00 | 5,23 | 0,00 | 0,87 | 1,41 | 1,41 | 0,05 | 0,07 | 0,13 |
| i4 | 1,68 | 0,82 | 1,56 | 0,00 | 5,23 | 1,19 | 0,43 | 1,41 | 1,41 | 0,87 | 0,00 | 0,05 | 0,13 | 0,07 | 0,05 | 0,06 | 0,06 | 0,17 | 0,00 |
| i5 | 1,68 | 1,68 | 0,82 | 5,23 | 0,00 | 5,23 | 1,19 | 0,87 | 1,41 | 1,41 | 0,87 | 0,00 | 0,07 | 0,13 | 0,07 | 0,05 | 0,06 | 0,06 | 0,17 |
| i6 | 0,82 | 1,68 | 1,68 | 1,19 | 5,23 | 0,00 | 5,23 | 0,00 | 0,87 | 1,41 | 1,41 | 0,87 | 0,05 | 0,07 | 0,13 | 0,07 | 0,17 | 0,06 | 0,06 |
| i7 | 1,56 | 0,82 | 1,68 | 0,43 | 1,19 | 5,23 | 0,00 | 0,05 | 0,00 | 0,87 | 1,41 | 1,41 | 0,06 | 0,05 | 0,07 | 0,13 | 0,00 | 0,17 | 0,06 |
| i8 | 5,23 | 1,19 | 0,43 | 1,41 | 0,87 | 0,00 | 0,05 | 0,13 | 0,07 | 0,05 | 0,06 | 0,00 | 0,06 | 0,17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i9 | 0,00 | 5,23 | 1,19 | 1,41 | 1,41 | 0,87 | 0,00 | 0,07 | 0,13 | 0,07 | 0,05 | 0,06 | 0,06 | 0,06 | 0,17 | 0,00 | 0,00 | 0,00 | 0,00 |
| i10 | 5,23 | 0,00 | 5,23 | 0,87 | 1,41 | 1,41 | 0,87 | 0,05 | 0,07 | 0,13 | 0,07 | 0,05 | 0,17 | 0,06 | 0,06 | 0,17 | 0,00 | 0,00 | 0,00 |
| i11 | 1,19 | 5,23 | 0,00 | 0,00 | 0,87 | 1,41 | 1,41 | 0,06 | 0,05 | 0,07 | 0,13 | 0,07 | 0,00 | 0,17 | 0,06 | 0,06 | 0,00 | 0,00 | 0,00 |
| i12 | 0,43 | 1,19 | 5,23 | 0,05 | 0,00 | 0,87 | 1,41 | 0,00 | 0,06 | 0,05 | 0,07 | 0,13 | 0,00 | 0,00 | 0,17 | 0,06 | 0,00 | 0,00 | 0,00 |
| i13 | 1,41 | 0,87 | 0,00 | 0,13 | 0,07 | 0,05 | 0,06 | 0,06 | 0,06 | 0,17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i14 | 1,41 | 1,41 | 0,87 | 0,07 | 0,13 | 0,07 | 0,05 | 0,17 | 0,06 | 0,06 | 0,17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i15 | 0,87 | 1,41 | 1,41 | 0,05 | 0,07 | 0,13 | 0,07 | 0,00 | 0,17 | 0,06 | 0,06 | 0,17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i16 | 0,00 | 0,87 | 1,41 | 0,06 | 0,05 | 0,07 | 0,13 | 0,00 | 0,00 | 0,17 | 0,06 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i17 | 0,13 | 0,07 | 0,05 | 0,06 | 0,06 | 0,17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i18 | 0,07 | 0,13 | 0,07 | 0,17 | 0,06 | 0,06 | 0,17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i19 | 0,05 | 0,07 | 0,13 | 0,00 | 0,17 | 0,06 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |

Separation distance 14 km

|  | v1 | v2 | v3 | v4 | v5 | v6 | v7 | v8 | v9 | v10 | v11 | v12 | v13 | v14 | v15 | v16 | v17 | v18 | v19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| I1 | 0,00 | 2,45 | 1,09 | 1,36 | 1,36 | 0,01 | 1,28 | 1,46 | 2,91 | 1,46 | 1,53 | 0,00 | 1,02 | 1,02 | 0,00 | 0,09 | 0,06 | 0,06 | 0,05 |
| I2 | 2,45 | 0,00 | 2,45 | 0,01 | 1,36 | 1,36 | 0,01 | 1,53 | 1,46 | 2,91 | 1,46 | 1,53 | 0,00 | 1,02 | 1,02 | 0,00 | 0,06 | 0,06 | 0,06 |
| I3 | 1,09 | 2,45 | 0,00 | 1,28 | 0,01 | 1,36 | 1,36 | 0,00 | 1,53 | 1,46 | 2,91 | 1,46 | 0,09 | 0,00 | 1,02 | 1,02 | 0,05 | 0,06 | 0,06 |
| I4 | 1,36 | 0,01 | 1,28 | 2,91 | 1,46 | 1,53 | 0,00 | 1,02 | 1,02 | 0,00 | 0,09 | 0,05 | 0,06 | 0,06 | 0,05 | 0,12 | 0,23 | 0,00 | 0,00 |
| I5 | 1,36 | 1,36 | 0,01 | 1,46 | 2,91 | 1,46 | 1,53 | 0,00 | 1,02 | 1,02 | 0,00 | 0,09 | 0,06 | 0,06 | 0,06 | 0,05 | 0,23 | 0,23 | 0,00 |
| I6 | 0,01 | 1,36 | 1,36 | 1,53 | 1,46 | 2,91 | 1,46 | 0,09 | 0,00 | 1,02 | 1,02 | 0,00 | 0,05 | 0,06 | 0,06 | 0,06 | 0,00 | 0,23 | 0,23 |
| I7 | 1,28 | 0,01 | 1,36 | 0,00 | 1,53 | 1,46 | 2,91 | 0,05 | 0,09 | 0,00 | 1,02 | 1,02 | 0,12 | 0,05 | 0,06 | 0,06 | 0,00 | 0,00 | 0,23 |
| I8 | 1,46 | 1,53 | 0,00 | 1,02 | 0,00 | 0,09 | 0,05 | 0,06 | 0,06 | 0,05 | 0,12 | 0,00 | 0,23 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| I9 | 2,91 | 1,46 | 1,53 | 1,02 | 1,02 | 0,00 | 0,09 | 0,06 | 0,06 | 0,06 | 0,05 | 0,12 | 0,23 | 0,23 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i10 | 1,46 | 2,91 | 1,46 | 0,00 | 1,02 | 1,02 | 0,00 | 0,05 | 0,06 | 0,06 | 0,06 | 0,05 | 0,00 | 0,23 | 0,23 | 0,00 | 0,00 | 0,00 | 0,00 |
| i11 | 1,53 | 1,46 | 2,91 | 0,09 | 0,00 | 1,02 | 1,02 | 0,12 | 0,05 | 0,06 | 0,06 | 0,06 | 0,00 | 0,00 | 0,23 | 0,23 | 0,00 | 0,00 | 0,00 |
| i12 | 0,00 | 1,53 | 1,46 | 0,05 | 0,09 | 0,00 | 1,02 | 0,00 | 0,12 | 0,05 | 0,06 | 0,06 | 0,00 | 0,00 | 0,00 | 0,23 | 0,00 | 0,00 | 0,00 |
| i13 | 1,02 | 0,00 | 0,09 | 0,06 | 0,06 | 0,05 | 0,12 | 0,23 | 0,23 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i14 | 1,02 | 1,02 | 0,00 | 0,06 | 0,06 | 0,06 | 0,05 | 0,00 | 0,23 | 0,23 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i15 | 0,00 | 1,02 | 1,02 | 0,05 | 0,06 | 0,06 | 0,06 | 0,00 | 0,00 | 0,23 | 0,23 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i16 | 0,09 | 0,00 | 1,02 | 0,12 | 0,05 | 0,06 | 0,06 | 0,00 | 0,00 | 0,00 | 0,23 | 0,23 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i17 | 0,06 | 0,06 | 0,05 | 0,23 | 0,23 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i18 | 0,06 | 0,06 | 0,06 | 0,00 | 0,23 | 0,23 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i19 | 0,05 | 0,06 | 0,06 | 0,00 | 0,00 | 0,23 | 0,23 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |

Separation distance 16 km

|  | v1 | v2 | v3 | v4 | v5 | v6 | v7 | v8 | v9 | v10 | v11 | v12 | v13 | v14 | v15 | v16 | v17 | v18 | v19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| I1 | 4,92 | 2,18 | 0,80 | 0,97 | 0,97 | 0,00 | 1,20 | 1,20 | 1,37 | 1,20 | 1,30 | 0,00 | 0,30 | 0,30 | 0,00 | 0,05 | 0,04 | 0,05 | 0,05 |
| I2 | 2,18 | 4,92 | 2,18 | 0,00 | 0,97 | 0,97 | 0,00 | 1,30 | 1,20 | 1,37 | 1,20 | 1,30 | 0,00 | 0,30 | 0,30 | 0,00 | 0,05 | 0,04 | 0,05 |
| I3 | 0,80 | 2,18 | 4,92 | 1,20 | 0,00 | 0,97 | 0,97 | 0,00 | 1,30 | 1,20 | 1,37 | 1,20 | 0,05 | 0,00 | 0,30 | 0,30 | 0,05 | 0,05 | 0,04 |
| I4 | 0,97 | 0,00 | 1,20 | 1,37 | 1,20 | 1,30 | 0,00 | 0,30 | 0,30 | 0,00 | 0,05 | 0,05 | 0,04 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 |
| I5 | 0,97 | 0,97 | 0,00 | 1,20 | 1,37 | 1,20 | 1,30 | 0,00 | 0,30 | 0,30 | 0,00 | 0,05 | 0,05 | 0,04 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 |
| I6 | 0,00 | 0,97 | 0,97 | 1,30 | 1,20 | 1,37 | 1,20 | 0,05 | 0,00 | 0,30 | 0,30 | 0,00 | 0,05 | 0,05 | 0,04 | 0,05 | 0,00 | 0,00 | 0,00 |
| I7 | 1,20 | 0,00 | 0,97 | 0,00 | 1,30 | 1,20 | 1,37 | 0,05 | 0,05 | 0,00 | 0,30 | 0,30 | 0,00 | 0,05 | 0,05 | 0,04 | 0,00 | 0,00 | 0,00 |
| I8 | 1,20 | 1,30 | 0,00 | 0,30 | 0,00 | 0,05 | 0,05 | 0,04 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| I9 | 1,37 | 1,20 | 1,30 | 0,30 | 0,30 | 0,00 | 0,05 | 0,05 | 0,04 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i10 | 1,20 | 1,37 | 1,20 | 0,00 | 0,30 | 0,30 | 0,00 | 0,05 | 0,05 | 0,04 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i11 | 1,30 | 1,20 | 1,37 | 0,05 | 0,00 | 0,30 | 0,30 | 0,00 | 0,05 | 0,05 | 0,04 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i12 | 0,00 | 1,30 | 1,20 | 0,05 | 0,05 | 0,00 | 0,30 | 0,00 | 0,00 | 0,05 | 0,05 | 0,04 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i13 | 0,30 | 0,00 | 0,05 | 0,04 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i14 | 0,30 | 0,30 | 0,00 | 0,05 | 0,04 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i15 | 0,00 | 0,30 | 0,30 | 0,05 | 0,05 | 0,04 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i16 | 0,05 | 0,00 | 0,30 | 0,00 | 0,05 | 0,05 | 0,04 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i17 | 0,04 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i18 | 0,05 | 0,04 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i19 | 0,05 | 0,05 | 0,04 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |

Separation distance 18 km

|  | v1 | v2 | V3 | v4 | v5 | v6 | v7 | v8 | v9 | v10 | v11 | v12 | v13 | v14 | v15 | v16 | v17 | v18 | v19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 2,26 | 1,81 | 0,29 | 0,17 | 0,17 | 0,00 | 1,28 | 1,31 | 1,21 | 1,31 | 0,96 | 0,21 | 0,00 | 0,00 | 0,17 | 0,05 | 0,05 | 0,05 | 0,08 |
| i2 | 1,81 | 2,26 | 1,81 | 0,00 | 0,17 | 0,17 | 0,00 | 0,96 | 1,31 | 1,21 | 1,31 | 0,96 | 0,17 | 0,00 | 0,00 | 0,17 | 0,05 | 0,05 | 0,05 |
| i3 | 0,29 | 1,81 | 2,26 | 1,28 | 0,00 | 0,17 | 0,17 | 0,21 | 0,96 | 1,31 | 1,21 | 1,31 | 0,05 | 0,17 | 0,00 | 0,00 | 0,08 | 0,05 | 0,05 |
| i4 | 0,17 | 0,00 | 1,28 | 1,21 | 1,31 | 0,96 | 0,21 | 0,00 | 0,00 | 0,17 | 0,05 | 0,07 | 0,05 | 0,05 | 0,08 | 0,00 | 0,00 | 0,00 | 0,00 |
| i5 | 0,17 | 0,17 | 0,00 | 1,31 | 1,21 | 1,31 | 0,96 | 0,17 | 0,00 | 0,00 | 0,17 | 0,05 | 0,05 | 0,05 | 0,05 | 0,08 | 0,00 | 0,00 | 0,00 |
| i6 | 0,00 | 0,17 | 0,17 | 0,96 | 1,31 | 1,21 | 1,31 | 0,05 | 0,17 | 0,00 | 0,00 | 0,17 | 0,08 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 |
| i7 | 1,28 | 0,00 | 0,17 | 0,21 | 0,96 | 1,31 | 1,21 | 0,07 | 0,05 | 0,17 | 0,00 | 0,00 | 0,00 | 0,08 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 |
| i8 | 1,31 | 0,96 | 0,21 | 0,00 | 0,17 | 0,05 | 0,07 | 0,05 | 0,05 | 0,08 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i9 | 1,21 | 1,31 | 0,96 | 0,00 | 0,00 | 0,17 | 0,05 | 0,05 | 0,05 | 0,05 | 0,08 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i10 | 1,31 | 1,21 | 1,31 | 0,17 | 0,00 | 0,00 | 0,17 | 0,08 | 0,05 | 0,05 | 0,05 | 0,08 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i11 | 0,96 | 1,31 | 1,21 | 0,05 | 0,17 | 0,00 | 0,00 | 0,00 | 0,08 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i12 | 0,21 | 0,96 | 1,31 | 0,07 | 0,05 | 0,17 | 0,00 | 0,00 | 0,00 | 0,08 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i13 | 0,00 | 0,17 | 0,05 | 0,05 | 0,05 | 0,08 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i14 | 0,00 | 0,00 | 0,17 | 0,05 | 0,05 | 0,05 | 0,08 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i15 | 0,17 | 0,00 | 0,00 | 0,08 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i16 | 0,05 | 0,17 | 0,00 | 0,00 | 0,08 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i17 | 0,05 | 0,05 | 0,08 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i18 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i19 | 0,08 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |

Separation distance 20 km

|  | v1 | v2 | v3 | v4 | v5 | v6 | v7 | v8 | v9 | v10 | v11 | v12 | v13 | v14 | v15 | v16 | v17 | v18 | v19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 1,94 | 1,51 | 0,00 | 0,00 | 0,00 | 1,66 | 1,47 | 1,38 | 1,52 | 1,38 | 0,28 | 0,07 | 0,22 | 0,22 | 0,07 | 0,05 | 0,05 | 0,06 | 0,00 |
| i2 | 1,51 | 1,94 | 1,51 | 1,66 | 0,00 | 0,00 | 1,66 | 0,28 | 1,38 | 1,52 | 1,38 | 0,28 | 0,07 | 0,22 | 0,22 | 0,07 | 0,06 | 0,05 | 0,06 |
| i3 | 0,00 | 1,51 | 1,94 | 1,47 | 1,66 | 0,00 | 0,00 | 0,07 | 0,28 | 1,38 | 1,52 | 1,38 | 0,05 | 0,07 | 0,22 | 0,22 | 0,00 | 0,06 | 0,05 |
| i4 | 0,00 | 1,66 | 1,47 | 1,52 | 1,38 | 0,28 | 0,07 | 0,22 | 0,22 | 0,07 | 0,05 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i5 | 0,00 | 0,00 | 1,66 | 1,38 | 1,52 | 1,38 | 0,28 | 0,07 | 0,22 | 0,22 | 0,07 | 0,05 | 0,06 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 |
| i6 | 1,66 | 0,00 | 0,00 | 0,28 | 1,38 | 1,52 | 1,38 | 0,05 | 0,07 | 0,22 | 0,22 | 0,07 | 0,00 | 0,06 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 |
| i7 | 1,47 | 1,66 | 0,00 | 0,07 | 0,28 | 1,38 | 1,52 | 0,05 | 0,05 | 0,07 | 0,22 | 0,22 | 0,00 | 0,00 | 0,06 | 0,05 | 0,00 | 0,00 | 0,00 |
| i8 | 1,38 | 0,28 | 0,07 | 0,22 | 0,07 | 0,05 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i9 | 1,52 | 1,38 | 0,28 | 0,22 | 0,22 | 0,07 | 0,05 | 0,06 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i10 | 1,38 | 1,52 | 1,38 | 0,07 | 0,22 | 0,22 | 0,07 | 0,00 | 0,06 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i11 | 0,28 | 1,38 | 1,52 | 0,05 | 0,07 | 0,22 | 0,22 | 0,00 | 0,00 | 0,06 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i12 | 0,07 | 0,28 | 1,38 | 0,05 | 0,05 | 0,07 | 0,22 | 0,00 | 0,00 | 0,00 | 0,06 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i13 | 0,22 | 0,07 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i14 | 0,22 | 0,22 | 0,07 | 0,06 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i15 | 0,07 | 0,22 | 0,22 | 0,00 | 0,06 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i16 | 0,05 | 0,07 | 0,22 | 0,00 | 0,00 | 0,06 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i17 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i18 | 0,06 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i19 | 0,00 | 0,06 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |

Separation distance 22 km

|  | v1 | v2 | v3 | v4 | v5 | v6 | v7 | v8 | v9 | v10 | v11 | v12 | v13 | v14 | v15 | v16 | v17 | v18 | v19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 1,60 | 1,19 | 0,00 | 5,92 | 5,92 | 1,26 | 1,18 | 1,00 | 1,26 | 1,00 | 0,00 | 0,05 | 0,07 | 0,07 | 0,05 | 0,05 | 0,07 | 0,18 | 0,00 |
| i2 | 1,19 | 1,60 | 1,19 | 1,26 | 5,92 | 5,92 | 1,26 | 0,00 | 1,00 | 1,26 | 1,00 | 0,00 | 0,05 | 0,07 | 0,07 | 0,05 | 0,18 | 0,07 | 0,18 |
| i3 | 0,00 | 1,19 | 1,60 | 1,18 | 1,26 | 5,92 | 5,92 | 0,05 | 0,00 | 1,00 | 1,26 | 1,00 | 0,05 | 0,05 | 0,07 | 0,07 | 0,00 | 0,18 | 0,07 |
| i4 | 5,92 | 1,26 | 1,18 | 1,26 | 1,00 | 0,00 | 0,05 | 0,07 | 0,07 | 0,05 | 0,05 | 0,00 | 0,07 | 0,18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i5 | 5,92 | 5,92 | 1,26 | 1,00 | 1,26 | 1,00 | 0,00 | 0,05 | 0,07 | 0,07 | 0,05 | 0,05 | 0,18 | 0,07 | 0,18 | 0,00 | 0,00 | 0,00 | 0,00 |
| i6 | 1,26 | 5,92 | 5,92 | 0,00 | 1,00 | 1,26 | 1,00 | 0,05 | 0,05 | 0,07 | 0,07 | 0,05 | 0,00 | 0,18 | 0,07 | 0,18 | 0,00 | 0,00 | 0,00 |
| i7 | 1,18 | 1,26 | 5,92 | 0,05 | 0,00 | 1,00 | 1,26 | 0,00 | 0,05 | 0,05 | 0,07 | 0,07 | 0,00 | 0,00 | 0,18 | 0,07 | 0,00 | 0,00 | 0,00 |
| i8 | 1,00 | 0,00 | 0,05 | 0,07 | 0,05 | 0,05 | 0,00 | 0,07 | 0,18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i9 | 1,26 | 1,00 | 0,00 | 0,07 | 0,07 | 0,05 | 0,05 | 0,18 | 0,07 | 0,18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i10 | 1,00 | 1,26 | 1,00 | 0,05 | 0,07 | 0,07 | 0,05 | 0,00 | 0,18 | 0,07 | 0,18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i11 | 0,00 | 1,00 | 1,26 | 0,05 | 0,05 | 0,07 | 0,07 | 0,00 | 0,00 | 0,18 | 0,07 | 0,18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i12 | 0,05 | 0,00 | 1,00 | 0,00 | 0,05 | 0,05 | 0,07 | 0,00 | 0,00 | 0,00 | 0,18 | 0,07 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i13 | 0,07 | 0,05 | 0,05 | 0,07 | 0,18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i14 | 0,07 | 0,07 | 0,05 | 0,18 | 0,07 | 0,18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i15 | 0,05 | 0,07 | 0,07 | 0,00 | 0,18 | 0,07 | 0,18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i16 | 0,05 | 0,05 | 0,07 | 0,00 | 0,00 | 0,18 | 0,07 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i17 | 0,07 | 0,18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i18 | 0,18 | 0,07 | 0,18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i19 | 0,00 | 0,18 | 0,07 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |

Separation distance 24 km

|  | v1 | v2 | v3 | v4 | v5 | v6 | v7 | v8 | v9 | v10 | v11 | v12 | v13 | v14 | v15 | v16 | v17 | v18 | v19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 1,23 | 0,78 | 3,75 | 1,48 | 1,48 | 1,21 | 0,84 | 0,22 | 0,81 | 0,22 | 0,00 | 0,05 | 0,05 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 |
| i2 | 0,78 | 1,23 | 0,78 | 1,21 | 1,48 | 1,48 | 1,21 | 0,00 | 0,22 | 0,81 | 0,22 | 0,00 | 0,05 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 |
| i3 | 3,75 | 0,78 | 1,23 | 0,84 | 1,21 | 1,48 | 1,48 | 0,05 | 0,00 | 0,22 | 0,81 | 0,22 | 0,06 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 |
| i4 | 1,48 | 1,21 | 0,84 | 0,81 | 0,22 | 0,00 | 0,05 | 0,05 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i5 | 1,48 | 1,48 | 1,21 | 0,22 | 0,81 | 0,22 | 0,00 | 0,05 | 0,05 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i6 | 1,21 | 1,48 | 1,48 | 0,00 | 0,22 | 0,81 | 0,22 | 0,06 | 0,05 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i7 | 0,84 | 1,21 | 1,48 | 0,05 | 0,00 | 0,22 | 0,81 | 0,00 | 0,06 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i8 | 0,22 | 0,00 | 0,05 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i9 | 0,81 | 0,22 | 0,00 | 0,05 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i10 | 0,22 | 0,81 | 0,22 | 0,05 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i11 | 0,00 | 0,22 | 0,81 | 0,06 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i12 | 0,05 | 0,00 | 0,22 | 0,00 | 0,06 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i13 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i14 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i15 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i16 | 0,06 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i19 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |

Separation distance 26 km

|  | v1 | v2 | v3 | v4 | v5 | v6 | v7 | v8 | v9 | v10 | v11 | v12 | v13 | v14 | v15 | v16 | v17 | v18 | v19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 0,80 | 0,00 | 1,53 | 1,21 | 1,21 | 1,54 | 0,00 | 0,00 | 0,00 | 0,00 | 0,08 | 0,05 | 0,05 | 0,05 | 0,05 | 0,23 | 0,00 | 0,00 | 0,00 |
| i2 | 0,00 | 0,80 | 0,00 | 1,54 | 1,21 | 1,21 | 1,54 | 0,08 | 0,00 | 0,00 | 0,00 | 0,08 | 0,05 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 |
| i3 | 1,53 | 0,00 | 0,80 | 0,00 | 1,54 | 1,21 | 1,21 | 0,05 | 0,08 | 0,00 | 0,00 | 0,00 | 0,23 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 |
| i4 | 1,21 | 1,54 | 0,00 | 0,00 | 0,00 | 0,08 | 0,05 | 0,05 | 0,05 | 0,05 | 0,23 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i5 | 1,21 | 1,21 | 1,54 | 0,00 | 0,00 | 0,00 | 0,08 | 0,05 | 0,05 | 0,05 | 0,05 | 0,23 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i6 | 1,54 | 1,21 | 1,21 | 0,08 | 0,00 | 0,00 | 0,00 | 0,23 | 0,05 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i7 | 0,00 | 1,54 | 1,21 | 0,05 | 0,08 | 0,00 | 0,00 | 0,00 | 0,23 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i8 | 0,00 | 0,08 | 0,05 | 0,05 | 0,05 | 0,23 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i9 | 0,00 | 0,00 | 0,08 | 0,05 | 0,05 | 0,05 | 0,23 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i10 | 0,00 | 0,00 | 0,00 | 0,05 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i11 | 0,08 | 0,00 | 0,00 | 0,23 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i12 | 0,05 | 0,08 | 0,00 | 0,00 | 0,23 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i13 | 0,05 | 0,05 | 0,23 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i14 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i15 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i16 | 0,23 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i19 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |

Separation distance 28 km

|  | v1 | v2 | v3 | v4 | v5 | v6 | v7 | v8 | v9 | v10 | v11 | v12 | v13 | v14 | v15 | v16 | v17 | v18 | v19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 0,00 | 0,00 | 1,24 | 1,29 | 1,29 | 1,24 | 0,00 | 0,22 | 0,00 | 0,22 | 0,05 | 0,05 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 |
| i2 | 0,00 | 0,00 | 0,00 | 1,24 | 1,29 | 1,29 | 1,24 | 0,05 | 0,22 | 0,00 | 0,22 | 0,05 | 0,06 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 |
| i3 | 1,24 | 0,00 | 0,00 | 0,00 | 1,24 | 1,29 | 1,29 | 0,05 | 0,05 | 0,22 | 0,00 | 0,22 | 0,00 | 0,06 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 |
| i4 | 1,29 | 1,24 | 0,00 | 0,00 | 0,22 | 0,05 | 0,05 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i5 | 1,29 | 1,29 | 1,24 | 0,22 | 0,00 | 0,22 | 0,05 | 0,06 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i6 | 1,24 | 1,29 | 1,29 | 0,05 | 0,22 | 0,00 | 0,22 | 0,00 | 0,06 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i7 | 0,00 | 1,24 | 1,29 | 0,05 | 0,05 | 0,22 | 0,00 | 0,00 | 0,00 | 0,06 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i8 | 0,22 | 0,05 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i9 | 0,00 | 0,22 | 0,05 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i10 | 0,22 | 0,00 | 0,22 | 0,06 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i11 | 0,05 | 0,22 | 0,00 | 0,00 | 0,06 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i12 | 0,05 | 0,05 | 0,22 | 0,00 | 0,00 | 0,06 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i13 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i14 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i15 | 0,06 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i16 | 0,00 | 0,06 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i19 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |

Separation distance 30 km

|  | v1 | v2 | v3 | v4 | v5 | v6 | v7 | v8 | v9 | v10 | v11 | v12 | v13 | v14 | v15 | v16 | v17 | v18 | v19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 0,00 | 2,93 | 1,19 | 1,35 | 1,35 | 0,78 | 0,00 | 0,06 | 0,10 | 0,06 | 0,05 | 0,06 | 0,06 | 0,06 | 0,17 | 0,00 | 0,00 | 0,00 | 0,00 |
| i2 | 2,93 | 0,00 | 2,93 | 0,78 | 1,35 | 1,35 | 0,78 | 0,05 | 0,06 | 0,10 | 0,06 | 0,05 | 0,17 | 0,06 | 0,06 | 0,17 | 0,00 | 0,00 | 0,00 |
| i3 | 1,19 | 2,93 | 0,00 | 0,00 | 0,78 | 1,35 | 1,35 | 0,06 | 0,05 | 0,06 | 0,10 | 0,06 | 0,00 | 0,17 | 0,06 | 0,06 | 0,00 | 0,00 | 0,00 |
| i4 | 1,35 | 0,78 | 0,00 | 0,10 | 0,06 | 0,05 | 0,06 | 0,06 | 0,06 | 0,17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i5 | 1,35 | 1,35 | 0,78 | 0,06 | 0,10 | 0,06 | 0,05 | 0,17 | 0,06 | 0,06 | 0,17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i6 | 0,78 | 1,35 | 1,35 | 0,05 | 0,06 | 0,10 | 0,06 | 0,00 | 0,17 | 0,06 | 0,06 | 0,17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i7 | 0,00 | 0,78 | 1,35 | 0,06 | 0,05 | 0,06 | 0,10 | 0,00 | 0,00 | 0,17 | 0,06 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i8 | 0,06 | 0,05 | 0,06 | 0,06 | 0,17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i9 | 0,10 | 0,06 | 0,05 | 0,06 | 0,06 | 0,17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i10 | 0,06 | 0,10 | 0,06 | 0,17 | 0,06 | 0,06 | 0,17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i11 | 0,05 | 0,06 | 0,10 | 0,00 | 0,17 | 0,06 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i12 | 0,06 | 0,05 | 0,06 | 0,00 | 0,00 | 0,17 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i13 | 0,06 | 0,17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i14 | 0,06 | 0,06 | 0,17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i15 | 0,17 | 0,06 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i16 | 0,00 | 0,17 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i19 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |

Separation distance 32 km

|  | v1 | v2 | v3 | v4 | v5 | v6 | v7 | v8 | v9 | v10 | v11 | v12 | v13 | v14 | v15 | v16 | v17 | v18 | v19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 2,27 | 1,39 | 1,54 | 0,95 | 0,95 | 0,00 | 0,08 | 0,06 | 0,06 | 0,06 | 0,05 | 0,23 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i2 | 1,39 | 2,27 | 1,39 | 0,00 | 0,95 | 0,95 | 0,00 | 0,05 | 0,06 | 0,06 | 0,06 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i3 | 1,54 | 1,39 | 2,27 | 0,08 | 0,00 | 0,95 | 0,95 | 0,23 | 0,05 | 0,06 | 0,06 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i4 | 0,95 | 0,00 | 0,08 | 0,06 | 0,06 | 0,05 | 0,23 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i5 | 0,95 | 0,95 | 0,00 | 0,06 | 0,06 | 0,06 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i6 | 0,00 | 0,95 | 0,95 | 0,05 | 0,06 | 0,06 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i7 | 0,08 | 0,00 | 0,95 | 0,23 | 0,05 | 0,06 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i8 | 0,06 | 0,05 | 0,23 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i9 | 0,06 | 0,06 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i10 | 0,06 | 0,06 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i11 | 0,05 | 0,06 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i12 | 0,23 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i13 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i14 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i15 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i16 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i19 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |

Separation distance 34 km

|  | v1 | v2 | v3 | v4 | v5 | v6 | v7 | v8 | v9 | v10 | v11 | v12 | v13 | v14 | v15 | v16 | v17 | v18 | v19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 1,33 | 1,20 | 1,25 | 0,00 | 0,00 | 0,00 | 0,06 | 0,05 | 0,04 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i2 | 1,20 | 1,33 | 1,20 | 0,00 | 0,00 | 0,00 | 0,00 | 0,05 | 0,05 | 0,04 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i3 | 1,25 | 1,20 | 1,33 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,05 | 0,05 | 0,04 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i4 | 0,00 | 0,00 | 0,06 | 0,04 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i5 | 0,00 | 0,00 | 0,00 | 0,05 | 0,04 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i6 | 0,00 | 0,00 | 0,00 | 0,05 | 0,05 | 0,04 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i7 | 0,06 | 0,00 | 0,00 | 0,00 | 0,05 | 0,05 | 0,04 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i8 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i9 | 0,04 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i10 | 0,05 | 0,04 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i11 | 0,05 | 0,05 | 0,04 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i12 | 0,00 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i13 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i14 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i15 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i16 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i19 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |

Separation distance 36 km

|  | v1 | v2 | v3 | v4 | v5 | v6 | v7 | v8 | v9 | v10 | v11 | v12 | v13 | v14 | v15 | v16 | v17 | v18 | v19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 1,21 | 1,37 | 0,89 | 0,00 | 0,00 | 0,12 | 0,05 | 0,05 | 0,05 | 0,05 | 0,09 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i2 | 1,37 | 1,21 | 1,37 | 0,12 | 0,00 | 0,00 | 0,12 | 0,09 | 0,05 | 0,05 | 0,05 | 0,09 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i3 | 0,89 | 1,37 | 1,21 | 0,05 | 0,12 | 0,00 | 0,00 | 0,00 | 0,09 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i4 | 0,00 | 0,12 | 0,05 | 0,05 | 0,05 | 0,09 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i5 | 0,00 | 0,00 | 0,12 | 0,05 | 0,05 | 0,05 | 0,09 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i6 | 0,12 | 0,00 | 0,00 | 0,09 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i7 | 0,05 | 0,12 | 0,00 | 0,00 | 0,09 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i8 | 0,05 | 0,09 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i9 | 0,05 | 0,05 | 0,09 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i10 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i11 | 0,09 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i12 | 0,00 | 0,09 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i13 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i14 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i15 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i16 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i19 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |

Separation distance 38 km

|  | v1 | v2 | v3 | v4 | v5 | v6 | v7 | v8 | v9 | v10 | v11 | v12 | v13 | v14 | v15 | v16 | v17 | v18 | v19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 1,55 | 1,32 | 0,01 | 0,18 | 0,18 | 0,06 | 0,05 | 0,06 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i2 | 1,32 | 1,55 | 1,32 | 0,06 | 0,18 | 0,18 | 0,06 | 0,00 | 0,06 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i3 | 0,01 | 1,32 | 1,55 | 0,05 | 0,06 | 0,18 | 0,18 | 0,00 | 0,00 | 0,06 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i4 | 0,18 | 0,06 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i5 | 0,18 | 0,18 | 0,06 | 0,06 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i6 | 0,06 | 0,18 | 0,18 | 0,00 | 0,06 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i7 | 0,05 | 0,06 | 0,18 | 0,00 | 0,00 | 0,06 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i8 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i9 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i10 | 0,06 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i11 | 0,00 | 0,06 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i12 | 0,00 | 0,00 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i13 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i14 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i15 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i16 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i19 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |

Separation distance 40 km

|  | v1 | v2 | v3 | v4 | v5 | v6 | v7 | v8 | v9 | v10 | v11 | v12 | v13 | v14 | v15 | v16 | v17 | v18 | v19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 1,55 | 1,32 | 0,01 | 0,18 | 0,18 | 0,06 | 0,05 | 0,06 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i2 | 1,32 | 1,55 | 1,32 | 0,06 | 0,18 | 0,18 | 0,06 | 0,00 | 0,06 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i3 | 0,01 | 1,32 | 1,55 | 0,05 | 0,06 | 0,18 | 0,18 | 0,00 | 0,00 | 0,06 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i4 | 0,18 | 0,06 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i5 | 0,18 | 0,18 | 0,06 | 0,06 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i6 | 0,06 | 0,18 | 0,18 | 0,00 | 0,06 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i7 | 0,05 | 0,06 | 0,18 | 0,00 | 0,00 | 0,06 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i8 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i9 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i10 | 0,06 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i11 | 0,00 | 0,06 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i12 | 0,00 | 0,00 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i13 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i14 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i15 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i16 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i19 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |

Separation distance 42 km

|  | v1 | v2 | v3 | v4 | v5 | v6 | v7 | v8 | v9 | v10 | v11 | v12 | v13 | v14 | v15 | v16 | v17 | v18 | v19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 0,72 | 0,00 | 0,00 | 0,05 | 0,05 | 0,05 | 0,07 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i2 | 0,00 | 0,72 | 0,00 | 0,05 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i3 | 0,00 | 0,00 | 0,72 | 0,07 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i4 | 0,05 | 0,05 | 0,07 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i5 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i6 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i7 | 0,07 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i8 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i9 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i10 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i11 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i12 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i13 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i14 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i15 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i16 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i19 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |

Separation distance 44 km

|  | v1 | v2 | v3 | v4 | v5 | v6 | v7 | v8 | v9 | v10 | v11 | v12 | v13 | v14 | v15 | v16 | v17 | v18 | v19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 0,00 | 0,00 | 0,07 | 0,05 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i2 | 0,00 | 0,00 | 0,00 | 0,05 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i3 | 0,07 | 0,00 | 0,00 | 0,06 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i4 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i5 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i6 | 0,05 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i7 | 0,06 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i8 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i9 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i10 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i11 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i12 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i13 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i14 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i15 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i16 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i19 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |

Separation distance 46 km

|  | v1 | v2 | v3 | v4 | v5 | v6 | v7 | v8 | v9 | v10 | v11 | v12 | v13 | v14 | v15 | v16 | v17 | v18 | v19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| i1 | 0,00 | 0,18 | 0,05 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i2 | 0,18 | 0,00 | 0,18 | 0,06 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i3 | 0,05 | 0,18 | 0,00 | 0,00 | 0,06 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i4 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i5 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i6 | 0,06 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i7 | 0,00 | 0,06 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i8 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i9 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i10 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i11 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i12 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i13 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i14 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i15 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i16 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i19 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |

Separation distance 48 km

|  | v1 | v2 | v3 | v4 | v5 | v6 | v7 | v8 | v9 | v10 | v11 | v12 | v13 | v14 | v15 | v16 | v17 | v18 | v19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| I1 | 0,08 | 0,06 | 0,05 | 0,07 | 0,07 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| I2 | 0,06 | 0,08 | 0,06 | 0,00 | 0,07 | 0,07 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| I3 | 0,05 | 0,06 | 0,08 | 0,00 | 0,00 | 0,07 | 0,07 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| I4 | 0,07 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| I5 | 0,07 | 0,07 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| I6 | 0,00 | 0,07 | 0,07 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| I7 | 0,00 | 0,00 | 0,07 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| I8 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| I9 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i10 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i11 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i12 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i13 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i14 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i15 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i16 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i19 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |

Separation distance 50 km

|  | v1 | v2 | v3 | v4 | v5 | v6 | v7 | v8 | v9 | v10 | v11 | v12 | v13 | v14 | v15 | v16 | v17 | v18 | v19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| I1 | 0,06 | 0,05 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| I2 | 0,05 | 0,06 | 0,05 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| I3 | 0,05 | 0,05 | 0,06 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| I4 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| I5 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| I6 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| I7 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| I8 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| I9 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i10 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i11 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i12 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i13 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i14 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i15 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i16 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i17 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i18 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |
| i19 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 | 0,00 |

# Text boxes

Electronic Communications Committee (ECC)

within the European Conference of Postal and Telecommunications Administrations (CEPT)

CDMA

CDMA

Figure 2