European Radiocommunications Committee (ERC)

within the European Conference of Postal and Telecommunications Administrations (CEPT)

European Radiocommunications Committee (ERC)

within the European Conference of Postal and Telecommunications Administrations (CEPT)

COMPATIBILITY STUDY BETWEEN THE FIXED SERVICE

AND MOTION SENSORS AT 10.5 GHz

Podebrady, May 1997

COMPATIBILITY STUDY BETWEEN THE FIXED SERVICE

AND MOTION SENSORS AT 10.5 GHz

1	INTRODUCTION

CEPT/ERC has developed Recommendation 12-05 for the frequency range 10.0-10.68 GHz on the harmonisation of this band for the fixed service (FS) (including ENG/OB).

A new CEPT/ERC recommendation is being developed covering, inter alia, the operation of short range devices within this frequency range. The existing recommendation T/R 60-01 (low power radiolocation equipment for detecting movement and for alert) suggests, as a second choice band, the use of 10.5-10.6 GHz with 500 mW EIRP systems. This band is only allocated in some countries for this application, sometimes with a lower EIRP.

This report deals with compatibility issues between the Fixed Service and motion sensors / interrogation systems in the frequency band 10.5-10.6 GHz.

2	EFFECT OF SUCH SYSTEMS ON FS RECEIVERS

Consider only one low power device equipment, with an interfering power of 500 mW, at a frequency falling within a radio relay receiver bandwidth.

A FS system at this frequency has the following characteristics :

Modulation : 4-PSK

Bit rate : 34 Mbit/s

Maximum long term admissible interference : -108 dBm

Bandwidth : 17 MHz

Antenna diameter : 1.6 m

Maximum antenna gain : 43 dB

Antenna pattern : according to ITU-R Rec.699-2

Interfering distances are derived according to the spherical earth diffraction model (ITU-R Rec.526-2). Additional obstacles and possible building attenuation are not taken into account in the calculation.

The result shows that the interfering distance ranges from 6 to 43 km, depending on the angle  between the wanted transmitter pointing direction and the interfering equipment pointing direction. The interfering area is around 400 km².

The interfering area also depends on the number of installed equipments which are assumed to increase significantly because of new interrogation equipments.

3	CONCLUSION

Sharing between full power (500mW EIRP) motion sensors/interrogation equipments and the fixed service or ENG/OB is not practicable. Note that CEPT/ERC Working Group Frequency Management defined the band 10-10.68 GHz as a harmonised frequency tuning range ‘Tuning range’ is the frequency range within which the equipment is capable of being tuned to any one in a range of specified frequencies whilst maintaining the required technical and operational characteristics. for ENG/OB systems.